## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Fate and behaviour of oil in
marine and shoreline environment

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
To understand the fate & behaviour of oil when spilled into the marine and shoreline environment.
Objective

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Physical and chemical processes will change oil properties and behaviour once spilled into the environment.
Referred to as “oil weathering”.
Oil weathering will influence selection of appropriate response strategies, affect operations and oil toxicity.
Oil weathering is influenced by important oil properties.
Oil Behaviour

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Specific gravity/oAPI:
  density
Viscosity:
  resistance to flow
Pour point:
  temperature below which oil does not flow
Important Oil Properties

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Volatility:
  propensity to evaporate
Flash point:
  temperature at which vapour will ignite
Asphaltene content:
  propensity to emulsify
Important Oil Properties

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Major processes:
Drifting
Spreading
Evaporation
Emulsification
Dispersion
Fate & Behaviour of Spilled Oil
Biodegradation
Dissolution
Photo-oxidation
Sedimentation
Shoreline interaction

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weathering Processes Over Time

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Spreading
Oil will spread & fragment on sea surface occupying a larger area.
Thickness of oil layer on sea surface will decrease over time, except in cases where oil emulsifies.
This process affects oil recovery rates as:
  Thin oil layer is difficult to recover
  Lower encounter rate as oiled area is increasing

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Spreading

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Drifting at Sea
Oil will drift at sea under the influence of currents and winds
100% current direction and speed, approximately 3% wind direction and speed

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Wind Effects
Wind
Wind
Wind

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Evaporation
Oil will release vapours in atmosphere.
Rate of emission will depend on ambient temperature, vapour pressure & concentration of volatile components.
Vapours are generally flammable and toxic (health and safety issue).
Evaporation will reduce volume of oil but increase oil viscosity.

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Emulsification
Water droplets can be incorporated into the oil layer by wave action forming an emulsion.
Can be stable or unstable
Asphaltene content is a good indication of an oil’s propensity to form stable emulsions (above 0.5%).
A major disadvantage for response:
  Increase oil viscosity
  Increase volume

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Emulsion

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Dispersion
Oil droplets will be naturally entrained in water column by wave action breaking oil slick into small droplets.
Small droplets have propensity to remain in suspension in water column, facilitating dilution and biodegradation.
  Larger droplets will resurface to reform an oil slick
Chemical dispersion using dispersants will enhance natural dispersion by promoting formation of small droplets.

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Dispersion
Braer Shetland Isles, UK, 1993

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Effects of Oil Weathering on Response
Safety
  Evaporation
Efficacy of response strategies
  Containment (e.g. spreading)
  In situ burning (e.g. losing ignitability by emulsification)
  Dispersants
  Skimmers
  Pumps

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Interactions
In most cases, oil slicks will reach coast.
Oil can become stranded on shoreline.
This process will be affected by shoreline wave exposure and by type of substrate.

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Man-made Shorelines
  Oil will generally penetrate deeply into permeable shorelines such as riprap/concrete tetrapods which limits the weathering process
  Oil will adhere to impermeable shorelines (concrete or steel wharves, etc.) with little penetration
  Oil may become trapped under pilings
  Not considered sensitive shoreline

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Interactions
Rocks and boulders
  Oil will generally penetrate deeply into permeable shorelines
  Deep penetration of oil limits the weathering process

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Interactions
Pebbles and cobbles beaches
  Oil will generally stick to surface of sediments.
  Oil can penetrate into interstices between sediment material.
    Generally, low viscosity oils can penetrate deeper into sediments than heavy oils.
  Clean-up can be difficult due to penetration.

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Interactions
Sand beaches
  Oil will generally remain on surface with minimal penetration – depending on surface grain size.
  Can be buried in layers by erosion and sand movements due to wind, waves or tides.
  Can mix with sand particles & sink in near shore environment or in intertidal zone.
  Can mix with fine mineral particles in intertidal zone forming small aggregates which will eventually be dispersed.

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Interactions
Mud flats and marshes
  Generally, oil penetration is not observed as these sediments are very compact and often flooded.
    Walking or heavy equipment can push oil into the sediments.
    Oil can penetrate into muddy shorelines via animals’ burrows.
  Oil can stick to vegetation.

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Interactions
Source: ITOPF
Source: Korea Coast Guard

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Subsea releases
Subsea releases can occur from sunken vessels or from a well blowout.
Oil will rise to surface forming a surface oil slick that will be exposed to normal oil weathering processes.
  Oil can re-surface far from spill source due to horizontal currents, density stratification and vertical turbulence mixing.
Smaller oil droplets can remain in water column, be dispersed under influence of subsea currents & subject to biodegradation.

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Conclusion
Weathering processes will change oil properties over time.
Will have a direct impact on safety & operations on effectiveness of spill equipment & clean-up techniques.

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?