## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Lesson 3.4 Technical Tools for Oil Spill Planning and Response

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Objective
To understand the technical aspects and tools available for oil spill preparedness and response especially oil behaviour, sensitivity maps and modelling.

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Technical Aspects
Contingency planning and response must be supported by sound technical knowledge and tools.
These will facilitate decision-making processes.
The main technical aspects to consider are:
  Oil fate and behaviour
  Oil spill modelling
  Sensitivity mapping.

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oil Fate and Behaviour

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oil Behaviour
Physical and chemical processes will change oil properties and behaviour once spilled into the environment.
These processes are referred to as “oil weathering”.
Oil weathering will influence the selection of appropriate response strategies, affect operations and oil toxicity.

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Important Oil Properties
Specific gravity/oAPI:
  density
Viscosity:
  resistance to flow
Pour point:
  temperature below which oil does not flow
Volatility:
  propensity to evaporate
Asphaltene content:
  propensity to emulsify

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Fate and Behaviour of Spilled Oil
Major processes:
Drifting
Spreading
Evaporation
Emulsification
Dispersion
Biodegradation
Dissolution
Photo-oxidation
Sedimentation
Shoreline interaction

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Drifting at Sea
Oil will drift at sea under the influence of currents and winds.
100% current direction and speed, approximately 3% wind direction and speed.

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Wind effects
Wind
Wind
Wind

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weathering Processes

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weathering Processes Over Time

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Effects of Main Weathering Processes
Increase in volume
Increase viscosity
EMULSIFICATION
Reduction in volume
Enhances biodegradation
DISPERSION
Reduction in volume
Increase viscosity
EVAPORATION

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oil Spill Modelling

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oil Spill Modelling
Useful tool for oil spill preparedness and response
Oil spill models will provide information on:
  Oil weathering
  Trajectory
Example of oil weathering and trajectory models:
  ADIOS and GNOME (NOAA)

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oil Spill Modelling
Types of models:
  Oil weathering (weathering over time)
  Stochastic (probability of impacts)
  Deterministic (oil trajectory over time)
  Hind-cast (identification of spill sources)
  3D (modelling of water column)

## Slide 16: Oil Spill Modelling
Types of models:
  Oil weathering (weathering over time)
  Stochastic (probability of impacts)
  Deterministic (oil trajectory over time)
  Hind-cast (identification of spill sources)
  3D (modelling of water column)
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 17: Oil Spill Modelling
Data requirements:
  Hydrodynamic data (surface currents, speed and direction)
  Wind data (speed and direction)
  Oil type
  Temperature (air and sea)
Caution:
  Output quality is highly dependent on data quality
  In a spill situation, modelling results must be validated by field observations
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 18: Sensitivity Maps
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 19: Sensitivity Maps
Essential tool for preparedness and response
Facilitate the decision-making process
Show locations of sensitive areas and their relative importance
Assist responders in identifying response priorities and potential consequences
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 20: Uses of Sensitivity Maps
For contingency planning:
    Location of sensitive areas
    Protection priorities
For spill response strategies:
    Dispersant prohibition areas
For shoreline protection strategies:
    Booming points
    Enhanced collection areas
For clean-up strategies:
    Beach types
    Access roads; near shore water depths
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 21: Sensitive Resources
Economic:
  industry
  tourism
  fishing areas
  aquaculture facilities
Social:
  residential areas
  recreational beaches
Environmental:
  Shoreline types
  Important areas (bird colonies; habitats, marshes; corals)
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 22: Priority Ranking
Sensitive areas can be ranked according to their relative sensitivity to oil and clean-up difficulty.
It provides a quick overview of highly sensitive areas.
Development of sensitivity maps:
  Working group with relevant stakeholders
  Compile information on resources and location
  Determine ranking
  Produce maps (GIS support).
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 23: High Priority Biological Resources
Marshes and mangroves | Highly vulnerable
Protected areas/ endangered species | Highly vulnerable
Sites of national and international importance for water birds | Highly vulnerable
Turtle nesting beaches | Highly vulnerable during breeding season
Coral reefs | Highly vulnerable
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 24: Sensitive Resources  Biological
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 25: Ranking of Human Use
High priority | Tourist areas: Recreational beaches Marinas Water intakes Fishing grounds
Medium priority | Ports and harbours Urban areas Industrial areas Fishing grounds
Low priority | Unused land
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 26: Sensitive Resources – Human Use
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 27: High Priority Shorelines
Marshes and mangroves
Reef flats which are exposed at low tide
Raised fossil reefs with undercuts
Boulder and cobble beaches
Pebble and cobble beaches
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 28: Sensitive Resources – Shorelines
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 29: Conclusion
Technical aspects are very important for oil spill preparedness activities and response
They are the basis for decision-making
Technical tools such as oil spill models and sensitivity maps will facilitate the decision- making process for managers
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 30
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?