## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Using Sorbents

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Objective
To understand the different types of sorbents and their use.

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Using Sorbents
Definition
Uses
Types
Forms
Advantages and disadvantages
Considerations

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Definitions
Sorbents are products or mixtures of products that are used to collect liquid oil through absorption and/or adsorption.
Absorbents: oil is soaked up and penetrates into the material.
Adsorbents: oil is attracted to and adheres to the surface of the material.

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Definitions
To be effective sorbents are :
Oleophilic (attracts oil)
Hydrophobic (repels water)
Do not sink
Easily recoverable

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Uses
Small spills
Recover final traces of oil “polishing”
Used to line boom and block any gaps
Used in areas where it is not possible to use a skimmer

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Protect area difficult to clean up
Recover effluents from clean-up operation
Filter oil in water column
Protect circulation path and working area
Clean up and decontaminate workers and equipment
Uses

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Types
Natural organic
Natural inorganic
Synthetic

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Forms
Bulk
Enclosed
Continuous
Fibre

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Organic
Peat moss
Straw/hay
Feathers
Corncobs
Sawdust
Wool
Hair
Other carbon based products

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Organic
Advantages:
  Use what is readily available in large amounts.
  Relatively low cost.
  Adsorb between 5 to 15 times their weight in oil.

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Organic
Disadvantages:
  Have a tendency to sink.
  Loose materials are difficult to control/recover and need to be contained.

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Organic
Straw bales used in a diesel spill

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Organic

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Inorganic
Vermiculite
Perlite
Clay
Volcanic ash
Sand
Snow

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Inorganic
Advantages:
  Use what is readily available in large amounts.
  Relatively low cost.
  Adsorb up to 20 times their weight in oil.

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Inorganic
Disadvantages:
  Loose materials are difficult to control/recover and need to be contained/not suitable for use on water.
  May be difficult to apply.
  Non bio-degradable.
  Wind can make it difficult to apply.

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Inorganic

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Synthetic
Polyurethane
Polypropylene
Polyethylene

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Pads, mats and rolls for various oil types
Sheets
Boom
Pom poms/snares
Synthetic

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sorbent Boom
Source: Fosse Liquitrol
Source: USCG

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Synthetic Pads
Source: Korea Coast Guard

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Pom Poms/Snare
Source: OSRL

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Synthetic
Advantages:
  Good retention capability  can adsorb/absorb up to 40 times their weight in oil
  Recover very little water
  May be reused
  Easy to deploy

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Disadvantages:
  Can create significant amounts of hazardous waste
  Heavy when saturated
  Not robust
Synthetic

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Considerations
Secondary contamination
Not intended for open sea
Cost
Storage and transportation

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Source: Korea Coast Guard
Avoid secondary contamination
Considerations

## Slide 28
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Ensure sorbents are contained
Source: Korea Coast Guard
Considerations

## Slide 29
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Practical Recommendations
Deploying sorbent boom
  deployed by boat or along shoreline
  can be joined together with fitted clips
  used to line other types of boom
  used to close gaps in other types of boom
  deployed as containment boom in small, calm areas
Recovering sorbent boom
  recover carefully section by section, putting into temporary storage container

## Slide 30
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Practical Recommendations
Deploying sorbent pads
can deploy by putting directly into floating oil or use as a contact barrier
ensure they are in a contained area to avoid secondary contamination
can be deployed from a boat or from shore
Recovering sorbent pads or rolls
can recover with pitchforks or nets
can collect and put into temporary storage unit

## Slide 31
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Practical Recommendations
Deploying granular sorbents
ensure they are in a contained area to avoid secondary contamination
apply directly to oil on land/docks
not for use on open water or in high winds
Recovering granular sorbents
recover with shovels, rakes
collect and put into temporary storage unit

## Slide 32
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Practical Recommendations
Deploying snare/pompom
may be tied in a continuous line/staked in place
Recovering snare/pompom
recover manually
collect on regular basis to prevent from becoming buried by sediment

## Slide 33
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Health and Safety
Always use proper PPE when deploying or recovering
Avoid contamination contact
Use proper lifting procedures
Be aware of the weight when recovering – saturated sorbents can become heavy

## Slide 34
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Summary
Use of sorbents can be effective under the proper conditions.
Use of sorbents must be carefully considered and managed to control cost, minimize waste and prevent secondary contamination.
Locally available organic sorbents are typically low cost compared to the more effective synthetic products.

## Slide 35
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?