## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Clean-up Techniques

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Objective
To understand the operational aspects of shoreline clean-up techniques.

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Aim
Recovery at sea is first priority because:
Less potential for ecological, socio-economic and cultural impacts in open waters
Shoreline clean-up is logistically more complex than oil recovery at sea
Costs increase dramatically when oil reaches shorelines
However, most oil spills reach the shoreline and cause visible pollution

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Overall Objective of Shoreline Clean-up
  Remove the oil or accelerate the natural recovery.
  The selection and correct application of clean-up techniques are therefore essential.
  Information generated by the SCAT survey(s) is a basic component of the decision process for setting response priorities, clean-up objectives and acceptable levels of treatment.

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Clean-up
Treatment standards (“end-points”) are based on:
  An accurate knowledge of the initial oiling conditions;
  The character of the stranded oil that is provided by the SCAT survey.
The decision to end the treatment should be based on goals or levels of effort established before the operation begins.

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Factors Affecting Shoreline Clean-up
Oil quantity
Oil characteristics:
  toxicity; viscosity
Prevailing on-site conditions:
  weather; season; tides; temperature; accessibility
Shoreline type

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Cross-Section of Beach Showing Shoreline Areas
Source: OSRL

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Stages of Shoreline Clean-up
Normally not an emergency – a project lasting weeks, months, years.
Stage 1. Removal of gross pollution and bulk oil
Stage 2. Removal of remaining stranded oil and oiled shoreline materials/debris
Stage 3. Final polishing/aesthetic treatment

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
NEBA
Net Environmental Benefit Analysis (NEBA)
Aims to decrease the overall effect of oil on the environmental and economic resources whilst achieving an acceptable standard of clean-up

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Recovery vs. Response
What is the working environment?
Will response activities accelerate natural recovery or will response activities delay natural recovery?
Are response activities possible from a safety perspective?

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Treatment Methods
  Natural recovery
  Physical methods:
    Washing
    Removal
    In situ Treatment
  Chemical and biological methods

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Recovery
Source: OSRL
Source: OSRL
High energy shoreline
Low energy shoreline

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
This group of methods involves a variety of washing or flushing techniques that can be used to move oil from the shore zone to a location for collection.
Flooding
Low-pressure washing
High-pressure washing
Physical Techniques  Washing

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Flooding
Source: OSRL

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Low-Pressure Washing
Source: ExxonMobil

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Low-Pressure Washing
Source: OSRL
Source: Korea Coast Guard

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
High Pressure Washing
Source: OSRL
Source: CEDRE

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Technique | Objective | Optimum use
Flooding | Flood a site so that mobile oil is lifted and carried downslope to a collection area | Most shoreline types Light to medium oils
Low-pressure, cold wash | Wash or flush oils toward a collection area using ambient sea, lake or river water at low pressure | Impermeable shorelines and marsh Light to medium oils
Low-pressure, warm/hot wash | Wash or flush oils at low pressure, using heated water, toward a collection area | Impermeable shorelines Light to medium oils
High-pressure, cold wash | Wash or flush oils toward a collection area using ambient sea, lake or river water at high pressure | Impermeable shorelines medium to heavy oils
High-pressure, warm/hot wash | Wash or flush oils at high pressure, using heated water, toward a collection area | Impermeable shorelines medium to heavy oils
Steam cleaning | Remove stains or dislodge thin layers of viscous oil from hard surface | Impermeable man-made structures Stains or heavy, weathered oils

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Operational Considerations
Washing oil and/or sediments downslope into the lower intertidal zones that have attached plant or animal communities should be avoided (especially if the flora/fauna were not initially oiled).
Can be avoided by working at high tide so oil is collected on water at times when these communities are below the water line.

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Operational Considerations
The mobilized or flushed oil and oiled sediment should be contained and collected.
Stranded oil on shorelines should also be contained to prevent contamination of adjacent shorelines by tides.
On marine coasts, only sea water should be used since fresh water can harm intertidal plants and animals.

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Operational Considerations
High-pressure water can dislodge/damage attached healthy organisms.
High-pressure action could emulsify the oil.
Extreme low temperatures may result in hoses freezing/formation of ice on shorelines.

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Physical Techniques: Removal
This group of physical methods involves removal of the oil or oiled material (sediments, debris, vegetation ) from the shore for disposal.
Manual
Vacuum systems
Mechanical
Vegetation cutting
Passive sorbents

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Manual Removal
Source: OSRL
Source: CEDRE

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Vacuum Systems
Source: OSRL
Source: Korea Coast Guard

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Mechanical Removal
Source: CEDRE
Source: OSRL

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Vegetation Cutting
Source: CEDRE
Source: ITOPF

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sorbents
Source: CEDRE
Source: CEDRE

## Slide 28
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Technique | Objective | Optimum use
Manual removal | Remove oil or oiled material (including oiled snow/ice) with manual labour and hand tool | Most shoreline types Small amounts of surface oil
Vacuum systems | Remove oil by suction from areas where it has pooled or collected in sumps | Light to medium, non-volatile, pooled or collected oil
Mechanical removal | Remove oil and oiled materials using mechanical equipment | Most fine to coarse-sediment beaches Large volumes of medium, heavy or solid oil
Vegetation cutting | Remove oiled stems to prevent remobilization of the oil or contact by animals and birds, or to accelerate the recovery of the plant. | Marshes, vegetated shorelines Where remobilization of oil will affect other resources.
Passive sorbents | Place sorbents in a fixed location(s) so that they pick up oil by contact | Any shoreline type Light to heavy, non-solid, non-volatile oils

## Slide 29
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Operational Considerations
Oily waste and debris removal
Minimize sediment removal
Source: OSRL

## Slide 30
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Operational Considerations
Traffic control:
  Can damage dunes, or other shorelines
  Can cause secondary contamination
  Minimize impact of personnel and vehicles on shorelines
Source: Korea Coast Guard
Source: Korea Coast Guard

## Slide 31
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Operational Considerations
Winter and summer conditions:
  Affects equipment operation (freezing/overheating)
  Health and safety of personnel from environmental hazards
Source: OSRL
Source: OSRL

## Slide 32
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Operational Considerations
Load-bearing capacity
  Shoreline must support equipment/personnel
Source: OSRL

## Slide 33
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Operational Considerations
Contain and collect sorbents:
  Sorbents must be contained and collected when saturated
Source: Korea Coast Guard

## Slide 34
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Physical Response Methods : In-situ Treatment
On-site treatment techniques to promote or increase weathering and natural degradation in situ.
    Mechanical tilling
    Sediment reworking/Surf washing
    Burning

## Slide 35
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Mechanical Tilling
Source: Korea Coast Guard
Source: Korea Coast Guard

## Slide 36
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sediment Reworking/Surf Washing
Source: CEDRE

## Slide 37
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Burning
Source: OSRL

## Slide 38
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Operational Considerations
Bearing capacity of substrate
Permit requirements
Level of oiling – tilling and surf washing are not used until gross oil has been removed.
Burning has additional health and safety issues.

## Slide 39
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Physical Response Methods: Chemical/Biological
This group includes:
      Shoreline cleaners
      Solidifiers
      Nutrient enrichment/Bioremediation
Facilitate removal of the oil from the shore zone.
Accelerate in situ weathering.

## Slide 40
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Cleaning Agents
Source: ITOPF

## Slide 41
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Bioremediation
Source: CEDRE

## Slide 42
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Operational Considerations
Additional PPE may be required during application.
No application of shoreline cleaners on sensitive substrates
Products and procedures must be approved
  Targeted application
  Use minimal quantities
  Prevent wash water from entering water courses
    Must use containment for shoreline cleaning agents/solidifiers.

## Slide 43
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Clean up Techniques by Shoreline Type
Man-made structures
Rocks and boulders
Cobbles, pebbles, shingle
Sand beaches
Muddy shores

## Slide 44
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Manmade Structures
 | Accessible | Inaccessible
Stage 1 | Skimmers/pumps Vacuum trucks Flushing | Manual Manual and sorbents
Stage 2 | Pressure washing Passive cleaning Dismantle (rarely) Natural cleaning | Natural cleaning Hand wiping
Stage 3 | Hand wiping Natural cleaning | Natural cleaning

## Slide 45
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Rock and Boulders
 | Accessible | Inaccessible
Stage 1 | Skimmers/pumps Vacuum trucks Flushing | Manual Manual and sorbents
Stage 2 | Pressure washing Sorbent materials Natural cleaning | Natural cleaning Hand wiping
Stage 3 | Natural cleaning Pressure washing Sand blasting (rarely) | Natural cleaning

## Slide 46
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Cobbles, Pebbles and Shingle
 | Accessible | Inaccessible
Stage 1 | Skimmers/pumps Vacuum trucks Flushing | Manual Manual and sorbents
Stage 2 | Flushing Surf/cobble washing Mechanical Natural cleaning | Natural cleaning Hand wiping
Stage 3 | Natural cleaning Surf/cobble washing Sand blasting (rarely) | Natural cleaning

## Slide 47
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sand Beaches
 | Accessible | Inaccessible
Stage 1 | Skimmers/pumps Vacuum trucks Manual/mechanical Trenching Flushing | Manual Manual and sorbents
Stage 2 | Flushing Surf/cobble washing Mechanical | Natural cleaning Manual
Stage 3 | Natural cleaning Surf washing Ploughing/tilling Beach cleaning machines Sand sieving | Natural cleaning

## Slide 48
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Muddy Shores
 | Accessible | Inaccessible
Stage 1 | Skimmers/pumps Vacuum trucks Flushing | Manual Manual and sorbents
Stage 2 | Flushing Manual | Natural cleaning Manual
Stage 3 | Natural cleaning | Natural cleaning

## Slide 49
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Saltmarshes/Mangroves
General considerations
  Difficult to access
  Possible options: inside
    Natural recovery
    Low-pressure washing
    Drainage and pumping
    Vegetation cutting
    Manual collection
  Possible option: in front and at sea
    Protection booms and sorbents
    Natural recovery

## Slide 50
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Subsurface Oil
  Oil may become buried in a variety of ways
  seaweed
  Wind-blown sand
  sand dune collapse during storm events
  mobile sediment due to wave action/tides
  permeates shoreline sediment

## Slide 51
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Subsurface Oil
  Locating and delineating subsurface oil
  pits in transects at right angles to shoreline
  trenches
  dogs
  core samples
  local knowledge and scientific expertise
Source: OSRL

## Slide 52
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Conclusion
Safety is always the first priority.
The selection and correct application of clean-up techniques are essential.
The methods will be based on oil quantity and characteristics, on-site conditions and shoreline type.
Shoreline workers must understand their role and task and work together safely.
Expert advice should be sought prior to undertaking treatment.

## Slide 53
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?