## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline site set-up, logistical and decontamination issues

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Objective
To understand the operational aspects of shoreline site set-up including logistical and decontamination issues.

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Logistics
Provides the equipment and services allowing the response effort to function on a daily basis.
The supply chain that logistics maintains keeps the spill response operations functioning.

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Logistics
Responsible for:
  Communications
  Medical support to incident personnel
  Food for incident personnel
  Supplies
  Facilities
  Ground support

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Logistics
Logistics ensures that the proper supplies and equipment are available.
This is a major task and must be done in order for operations to begin.
  Example: Personnel need PPE before work can begin.
  Example: Vessels need to refuel regularly to continue operations.
  Example: Operations needs boom and all related boom accessories to protect.

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Supply Chain
  Communications
  Distributes and maintains communications equipment

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Supply Chain
  Medical
  Provides first aid and light medical treatment services and equipment
  May need to de-contaminate

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Supply Chain
  Food
  Food and potable water
  Obtains equipment and supplies to operate food service facilities
Source: CEDRE

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Supply Chain
  Supply
  Assists in determining the type and amount of supplies needed to support the incident
  Orders, receives, stores and distributes supplies
  Services equipment
  Places all resource orders
  Maintains inventory of supplies and equipment

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Supply Chain  Support Branch
  Facilities unit
  Sets up and maintains facilities
  Provides managers for base and camps
  Provides facility security and maintenance services (sanitation, lighting, clean-up, decontamination supplies)
Source: Korea Coast Guard

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Supply Chain
  Ground support
  Arranges for and documents the fueling and maintenance of ground resources
  Arranges for transportation of personnel, supplies, food and equipment
Source: Korea Coast Guard
Source: Korea Coast Guard

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Staging Area
Temporary location where equipment, personnel and other resources are staged while waiting for tactical assignments
Strategically located to supply the response operations
Typically close to response operations (may be limited by access to property, physical geography, etc.)

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Staging Area
Requires a large, flat area with access for equipment such as boats, heavy machinery, spill equipment, rest facilities, parking area, etc.
A decontamination area where oiled personnel and equipment can be cleaned/disposed of

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Staging
Source: ITOPF

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Daily Briefing
Source: Korea Coast Guard

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Staging
Source: Korea Coast Guard

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Source: Korea Coast Guard

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Decontamination
Part of the Health and safety plan
Critical for the health and safety of response personnel
Critical to avoid secondary contamination by response personnel or other spill vehicles and vessels
Logistics procures the decon supplies and equipment

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Decontamination
  Personnel
  Vessels
  Vehicles, i.e. trucks, ATVs
  Heavy equipment
  Spill equipment
    Skimmers
    Boom
    Pumps/hoses
    Storage tanks

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Decon Plan
Description and location of decon facilities
List of decon equipment required
PPE for the personnel doing the decon
Decon procedures for specific materials
Procedures to prevent secondary contamination
Procedures to prevent secondary contamination for personnel removing oiled PPE

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Decon Plan
Safe disposal methods for various materials that cannot be decontaminated, i.e. disposal coveralls, gloves, sorbents
Revisions for changes in site conditions

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Decon Facilities
Decon should be done in stages, moving either from a cold zone (clean, support), through a warm zone (contamination) to a hot zone (exclusion) or vice versa
Hot Warm Cold

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Decontamination Facilities
Hot Zone
Dirty/work area: all oil stays in this zone
Warm Zone
Clean down area: Controlled entrance/exits with decontamination
Cold Zone
Waste removal vehicles can enter to remove collected waste from temporary storage sites
Source: OSRL

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Typical Decon Layout
Source: OSRL

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Decon  Personnel
Decon facilities set up for responders
  Remove oiled PPE in a controlled environment
  Washing facilities
  Storage facilities for cleaned PPE and clean clothing
  Waste facilities for disposable PPE
Proper decon facilities for PPE means it stays in good conditon longer, is more cost effective and reduces strain on the supply chain

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Decon  Personnel
Avoid contamination contact
Practice good hygiene and decontamination procedures
Understand the product characteristics and use PPE appropriately

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Decon  Personnel
Important for personnel to use proper PPE and decon procedures to avoid:
  Inhalation  Respiratory protection during initial response (vapours) and while pressure washing (mists)
  Ingestion  Wash up prior to eating and drinking (smoking)
  Aspiration  Fall into product and or during mist generation
  Absorption  Direct skin contact usually through improper glove/sleeve interface

## Slide 28
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Control Entrance/Exit
Source: CEDRE

## Slide 29
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Source: CEDRE
Source: Swedish Coast Guard
Decon

## Slide 30
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Vehicles and Heavy Equipment
Important to avoid secondary contamination by vehicles.
Transport cleaning stations need to be set up to prevent oil from being transferred to roads or other public places.
A lined containment area where vehicles can drive onto and be cleaned, including tyres.

## Slide 31
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Decon
Source: CEDRE

## Slide 32
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Equipment Cleaning

## Slide 33
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Vessels
Oiled vessels must be kept in a “hot” area during spill operations that should be boomed to prevent contamination of clean areas.
Boom gates can be used to allow vessels to move between boomed areas.
Vessels must be decontaminated when ready to demobilize or move vessel to another location.

## Slide 34
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Vessels
Vessel washing stations can be set up with lined containment areas to clean hull and decks.
Oily wash water must be contained and collected.

## Slide 35
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Vessel-on-Water

## Slide 36
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Scraping oil from deck
Adding sand….
Heavily oiled ships
Heavily oiled ships

## Slide 37
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Small Craft - On Water

## Slide 38
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Small Craft - On land

## Slide 39
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
A beach supervisor is appointed
Work forces of max. 10 people
Team leader for each group
Team leaders refer to beach supervisor
Each team has special functions/beach section
Activities must be clearly defined
Organization and Tasks of a Clean-up Operation

## Slide 40
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Make record of all works carried out: report to beach supervisor.
All personnel must wear protective work clothes and other safety equipment.
Team leader responsible for team following safety and health regulations.
Team Leader Guidelines

## Slide 41
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Provision of all equipment required
Breaks, refreshments
Control of all vehicle traffic
Cleaning of all equipment after use and making ready for next day
Ensuring that all personnel have received full operational safety briefing
Keeping public at safe distance
Contact with the mass media (if authorized)
Beach Supervisor Guidelines

## Slide 42
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Beach supervisor must:
agree with OSC the acceptable cleaning status to be achieved;
specify tasks for each team;
outline procedures to be followed for each team;
specify equipment to be used;
designate vehicle traffic and storage areas;
define working periods;
ensure safety checklist is given to team leaders.
Making an Operational Plan

## Slide 43
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Beach supervisors and team leaders:
Communication systems defined and checked
Tools not left scattered on beach
Routes for trucks defined
All work areas illuminated during operations
All personnel equipped with safety clothing
All personnel briefed on safety hazards
If explosion risk, all equipment is spark-free or explosion safe (e.g. motors, diesel engines)
Health and Safety Requirements

## Slide 44
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Team leaders and beach supervisors:
If chemicals used, PPE must be available (eye washes, masks, etc.).
Proper cleaning and maintenance of all equipment must be carried out.
Familiarity with safety procedures in case of injury.
Pump and skimmer personnel instructed about proper use and potential risks and hazards.
Health and Safety Requirements

## Slide 45
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Conclusions
Logistics is critical to the response effort.
The supply chain must maintained to avoid “bottlenecks”  even small breaks in this chain can suspend operations e.g. fuel or drinking water.
Staging and decontamination facilities are required immediately to allow personnel to safely leave the spill site and to maintain equipment.
Shoreline workers must understand their role and task and work together safely.

## Slide 46
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?