## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Implementing Waste Management

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Objective
To understand the importance of implementing waste management best practices in the field when responding to an oil spill.

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Issues
Planning
Types of waste
Temporary/intermediate storage
Transportation
Final disposal

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
How Much Waste?
750 m3
3,750 m3
3,000 m3
750 m3 liquid waste for disposal
30,000 m3 solid waste for disposal
Impact the shoreline (mixed with 10x its volume of debris)
20% Recovered at sea
Emulsified (80% water)
25% Evaporated
For 1,000 m3

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste from Crude Oil Spills
Year | Incident name | Oil spilled (tonnes) | Liquid collected (tonnes) | Solid material collected (tonnes) | Total waste collected (tonnes) | Ratio of material collected to spilled oil
1978 | AMOCO CADIZ | 227,000 | 100,000 | 100,000 | 200,000 | 0.9
1989 | EXXON VALDEZ | 37,000 | 97,500 | 38,800 | 136,300 | 3.7
1993 | BRAER | 86,200 | - | 2,000 | 2,000 | 0.02
1995 | SEA PRINCE | 5,500 | 2,000 | 5,100 | 7,100 | 1.3
1996 | SEA EMPRESS | 72,370 | 25,000 | 11,000 | 36,000 | 0.5
2004 | ATHOS 1 | 900 | 200 | 6,700 | 6,900 | 7.7
2007 | HEBEI SPIRIT | 10,900 | 2,610 | 37,620 | 40,230 | 3.7
2010 | DEEPWATER HORIZON | 780,000 | 162,260 | 89,200 | 251,460 | 0.3
Source: ITOPF

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste from Fuel Oil Spills
Year | Incident name | Oil spilled (tonnes) | Liquid collected (tonnes) | Solid material collected (tonnes) | Total waste collected (tonnes) | Ratio of material collected to spilled oil
1980 | TANIO | 13,500 | - | 28,000 | 28,000 | 2.1
1988 | AMMAZZONE | 2,100 | - | 13,000 | 13,000 | 6.2
1997 | NAKHODKA | 6,200 | - | 50,000 | 50,000 | 8.1
1997 | NISSOS AMORGOS | 3,600 | - | 40,000 | 40,000 | 11.1
1999 | VOLGONEFT 248 | 1,279 | - | 4,500 | 4,500 | 3.5
1999 | ERIKA | 19,800 | 1,100 | 200,000 | 201,100 | 10.2
2001 | BALTIC CARRIER | 2,550 | 965 | 10,750 | 11,715 | 4.6
2002 | PRESTIGE | 63,000 | 50,000 | 159,300 | 209,300 | 3.3
2006 | SOLAR 1 | 2,081 | - | 5,010 | 5,010 | 2.4
2007 | VOLGONEFT 139 | 2,000 | 200 | 79,740 | 79,940 | 40.0
Source: ITOPF

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Comparison of Quantities
Source: IPIECA/IOGP

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste management challenges can seriously affect the response efficiency

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Hierarchy
Response priority should be to minimize waste production as much as possible!
Reduce
Reuse
Recycle
Recover
Dispose

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Types of Waste
Liquid:
Oil
Oil/water mixture
Emulsion
Solid:
Oiled sediment
Oiled driftwood/seaweed
Oiled debris
Cleaning materials
  Sorbent materials
  PPE

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Temporary and Intermediate Storage
Significant quantities of waste are generated during clean-up operations
  Mainly by recovery at sea and shoreline clean-up
  Less waste generated by using dispersants and in situ burning
If no storage is available, recovery operations will have to stop!
Important to think about the waste stream before beginning oil recovery operations

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Stream
Source: OSRL

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Temporary Storage
At sea:
Barges
Vessel tanks
Floating tanks
Onshore:
Skips
Portable tanks
Drums
Lined excavated (temporary) pits
Plastic bags

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
At-Sea Storage
Source: CEDRE

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
At-Sea Storage
Source: Korea Coast Guard

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Onshore Storage
Source: OSRL

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Temporary Storage
Prevent secondary contamination
  Ensure storage is water/oil-proof to avoid leakage
  Ensure site is suitable for temporary containers
    Flat with stable ground
    Easy access for heavy equipment
    Close to recovery sites
  Install liner under temporary containers
  Keep absorbent material nearby in case of a small spill
  Ensure all vehicles used for waste transportation are decontaminated before leaving response sites

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Temporary Storage
Source: Korea Coast Guard

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Prevent Secondary Contamination
Hot Zone
Dirty/work area: all oil stays in this zone
Warm Zone
Clean down area: Controlled entrance/exits with decontamination
Cold Zone
Waste removal vehicles can enter to remove collected waste from temporary storage sites
Source: OSRL

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste must be Separated!
By waste type
  Oil
  Solids (debris)
  Liquids
  PPE
  others
Ensure training and monitoring of working crews
Ensure appropriate containers are in place for all waste types at recovery sites

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste must be Separated!
Source: OSRL
Source: ITOPF

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oiled Debris
Source: OSRL

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oiled PPE
Source: OSRL

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Transportation
Waste in temporary storage must be transported for final disposal.
These can be transported by various means:
  Trucks
  Loaders
  Boats
  Helicopters.
Containers must be adapted for transport
  Resistance
  Weight.

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Think about Transfers!
Source: OSRL

## Slide 28
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Transportation
Source: OSRL

## Slide 29
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Transportation
Source: ITOPF

## Slide 30
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Hierarchy
Source: IPIECA

## Slide 31
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Final disposal
Reuse (after treatment)
Direct disposal - landfill
Stabilization - quick lime, road construction
Incineration
Land farming and composting

## Slide 32
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Treatment and Disposal Methods
Source: IPIECA

## Slide 33
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Summary of Options
Source: IPIECA

## Slide 34
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Conclusion
Waste management can affect response effectiveness
Minimize – segregate
Think about the waste stream
    Storage
    Transfer
    Transport
Field personnel must be aware of good practice for waste management

## Slide 35
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?