## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Containment and Protection

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Objective
To understand the operational aspects for containment and protection boom deployment including support equipment and anchoring techniques.

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Outline
Boom characteristics
Boom types
Boom deployment
Boom anchoring
Support equipment

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom
Physical barrier to:
  Stop spreading
  Concentrate oil
  Protect sensitive resources
Many types

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Characteristics

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Key Characteristics of Boom
Size
Freeboard
Draft
Buoyancy ratio
Strength
Ease of deployment

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Key Components of Boom

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Types

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Types
Curtain boom
  Solid floatation
  Self inflating
  Inflatable
Shore seal boom

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Curtain Boom
Flotation member filled with air, inert gas, solid foam or granulated foam.
Flexible skirt which can move independently of flotation member.
Buoyancy ratio between 5:1 – 20:1.
Air filled booms: easy to clean but slower to deploy than solid booms.
Storage: small for air filled; large for solid foam filled booms.

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Solid Flotation Boom

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Solid Flotation Fence Boom

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Self Inflating Boom

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Inflatable Boom

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Inflatable Boom

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shore Seal Boom
Specially designed to keep the oil in the inter-tidal zone.
Unique – cannot be replaced by other boom types.
Must be handled with care to prevent tearing the bottom.
Can be connected to floating containment booms.
Ensure boom in position before commencing to fill ballast chambers.
Ensure extends above the high water mark.

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shore Seal Boom

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shore Seal Boom – Low Water
Air
Water
Low Tide

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shore Seal Boom – High Water
Air
Water
High tide

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shore Seal Boom

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shore Seal Boom

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sorbent Boom
Sorbent material in cylindrical shape
Deployed like a boom
May have clips that allow sections to be joined together
May have skirts

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sorbent Boom

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Selection
Boom selection based on
  Environmental conditions
  Performance characteristics
  Convenience characteristics

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Selection

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Selection

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Limitations of Boom
Deployment takes time during which oil spreads
Fail in strong currents and winds
Easily damaged
Require extensive logistical support
Require regular maintenance
Mooring and anchoring problems
Close-off water areas, hindering boat movement

## Slide 28
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sea State and Boom Size

## Slide 29
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Failure
Source: Fingas, “The Basics of Oil Spill Clean-up” 2001

## Slide 30
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Failure

## Slide 31
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Deployment

## Slide 32
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Deployment from Vessel
Deployment operation steps:
  Secure equipment to the deck - boom reels, power packs, or other auxiliary equipment as required.
  Attach towing equipment to outboard section of boom – towing bridle/towing paravane, towline.
  Attach a float/buoy to the end of the towline for easier retrieval.
  Pay out boom reel, deploying the boom sections over the stern.
Essential to secure equipment properly on board vessel before operation.

## Slide 33
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Deployment from Vessel
Deployment operation steps:
  For inflatable boom each section is inflated on the deck as boom is paid out.
  When inflating boom sections, ensure boom is secure with a safety chain/cable before workers insert blowers to fill valves for safety.
  Vessel should deploy into the wind/current allowing boom to stream astern without wrapping around stern or fouling the propellers.
  Connect the boom to the auxiliary vessel – the float/buoy on towline can be used for easier retrieval.

## Slide 34
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Deployment from Vessel
Boom reel operator must use signaller and have a clear line of sight.
Be aware of pinch points.
Be aware of working near the stern of the vessel.
Understand man overboard procedures.

## Slide 35
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Deployment from Vessel
Safest deployment uses a main vessel alone  reduces risk.
If two vessels are conducting boom operations together, communication between the two vessels is essential for successful and safe operations.
Vessels must coordinate speed and power.

## Slide 36
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Deployment from Vessel
The steps for boom deployment are reversed.
Boom is spooled onto reel as it is recovered.
Inflatable boom is deflated as each section comes on board ensuring a safety chain/cable is attached before workers insert hose into valve.
Be aware of pinch points.

## Slide 37
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Deployment

## Slide 38
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Deployment from Shoreline
Deployment operation steps:
  Secure equipment  boom reels, power packs, or other auxiliary equipment as required.
  Attach towing equipment to outboard section of boom – towing bridle/towing paravane, towline if boom is being pulled out by a vessel.
  Clear shoreline of debris that can damage the boom/use chafing mats.
  Pay out boom reel/boom by hand.
Essential to secure equipment properly before operation whether beach or man-made structure.

## Slide 39
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Deployment Approach
Source: National Spill Control School

## Slide 40
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
3
Boom Deployment Approach

## Slide 41
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Recovery from a Shoreline
The steps for boom deployment are reversed.
Boom is spooled onto reel as it is recovered.
Ensure boom isn’t being damaged by dragging over debris/rough shorelines.
Be aware of pinch points.

## Slide 42
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Standard Boom Configurations
On-water containment and recovery
Single vessel
Two vessels
  J-configuration
  U-configuration
Three vessels

## Slide 43
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Vessel Operations
Two main categories:
  Purpose built or adapted response vessels
  Vessels of opportunity (VOO).
All vessels must be fit for purpose and approved by the relevant authorities (maritime administration, etc.).
VOO may be fitted with response equipment and trained personnel.
Local VOOs will have local knowledge.

## Slide 44
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Single Vessel Configurations

## Slide 45
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Single Vessel Configurations

## Slide 46
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Two Vessel - J-Configuration

## Slide 47
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Two Vessel - U-Configuration

## Slide 48
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Three Vessel - U-Configuration

## Slide 49
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Three Vessel - U-Configuration

## Slide 50
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Containment
Encircle a stricken vessel.
Contain spill from a terminal.
Prevent or minimize contact with shoreline.
Increase thickness of oil to facilitate effective skimming operations.
Contain previously stranded oil.

## Slide 51
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Containment

## Slide 52
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Redirection
Direct oil away from a sensitive site or shoreline area.
Or direct oil towards a shoreline.

## Slide 53
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Redirection

## Slide 54
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Redirection

## Slide 55
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Redirection

## Slide 56
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Redirection

## Slide 57
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Exclusion
Booming around a sensitivity to exclude oil from sensitivity
  Examples: Fish farm, inlets, water intakes, marsh

## Slide 58
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Exclusion
Source: OSRL

## Slide 59
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Chevron Booming
Open chevron booming
Closed chevron
booming

## Slide 60
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Deflectors
Using
boom deflectors
Source: Hansen and Coe

## Slide 61
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Anchoring

## Slide 62
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Anchoring Systems
Depends on:
Forces working on the boom
Current direction
Length of boom
Size of vessel

## Slide 63
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Anchoring
Requires knowledge about:
Seabed
Current direction(s)
Current velocity
Water depth

## Slide 64
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Anchoring Systems
Knowledge of local seabed condition is essential.
Current in one direction requires anchors on one side - against current.
Current from both sides requires anchors on both sides.

## Slide 65
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Rope length from anchor to mooring buoy must be 2 times water depth.
Rope length from anchor to anchor buoy must be 2 times water depth.
Anchor size = 20100 kg and holding power = 30 times its weight.
Anchor chain keeps anchor rod down.
Anchoring Systems

## Slide 66
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Deployment Angle
Source: OSRL

## Slide 67
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Common Anchor Types
Anchor Type | Soft Soils | Hard Soils
Danforth LWT | 12.6 | 31.6
STATO NAVMOOR | 27.7 | 25 – 33
Navy Stockless | 3.5 | 11
Anchor holding power
for 45kg (~100 lbs)
Source: U.S. Navy

## Slide 68
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Typical Anchoring Arrangement

## Slide 69
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Anchoring

## Slide 70
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Anchoring
Use of piles/stakes on shoreline

## Slide 71
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Anchoring V-Shape Boom
Anchoring
V-shaped boom
in
mid-channel

## Slide 72
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Anchoring J-Shape Boom
Anchoring
J-shaped boom

## Slide 73
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Multiple Anchors
Multiple
anchor
deployment

## Slide 74
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Tidal Entrances
Boom that protects during flood tide
Boom that protects during ebb tide
Position of boom B during flood tide
Source: National Spill Control School

## Slide 75
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Harbour Flow Patterns  Flood

## Slide 76
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Harbour Flow Patterns  Flood

## Slide 77
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Tidal Compensator

## Slide 78
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Support Equipment

## Slide 79
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Support Equipment
Boom connectors
Towing bridles and paravanes
Anchor buoys/cans
Boom magnets
Boom lights

## Slide 80
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Connectors
Various types of connectors for different types, sizes and manufacturers.
Must be compatible to connect, disconnect, add other attachments.
Can have adaptors made but may be difficult to get at the time of spill.

## Slide 81
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Towing Bridles/Paravanes
For towing boom – provides strong point.
Keeps boom from twisting.
Guides through the water.
Must be compatible with boom connector.
Boom must be towed very slowly, typically less than 1 knot.

## Slide 82
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Anchor Buoys/Cans
Can be inserted between sections of boom to take the force/stress of the anchor.
Can be fitted with reflective tape or anchor lights.

## Slide 83
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Magnets
Heavy duty magnets allow boom to be attached to steel hull of vessel or steel wharf.
Allows containment of a section of a vessel or wharf as opposed to complete encirclement.
Creates a good seal to side of vessel – sorbent boom can be placed in any gaps.
Limited in amount of stress that can be on boom without magnet letting go.
Requires approval from vessel master to place on hull.
Safety hazard near pacemakers.

## Slide 84
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Lights
Boom lights allow boom to be illuminated at night/restricted visibility where boom is a hazard to navigation.
Solar lights.

## Slide 85
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Vane
Can be deployed from shore or a vessel to create a single vessel sweep.
Source: ORC AB

## Slide 86
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Storage
Boom can be stored on a reel, in containers, in trailers.
Stored clean and dry, protected from elements, sunlight and pests (rodents, racoons, etc.).
Stored in a ready state.
Source: CEDRE

## Slide 87
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Cleaning
Boom that has been used should be rinsed with fresh water and stored dry.
Boom that has been oiled should be decontaminated properly by washing manually or in a boom washing machine.
Boom should be inspected for damage before being stored.

## Slide 88
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?