## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oil Skimmers

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
AIM
Knowledge of common types of skimmers
Knowledge of common types of pumps and transfer systems

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Skimmers

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Skimmer
A skimmer is a mechanical device specifically designed for the removal of oil from the surface of water without altering its physical and/or chemical characteristics.

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Skimmer Types
Weir skimmers
Oleophilic skimmers
Vacuum skimmers
Mechanical skimmers

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Skimmer Selection Matrix
Refer to ExxonMobil
Oil Spill Response Field Guide
Chapter 9

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weir Skimmer
Advantages :
High recovery rate
Wide viscosity range
Simple maintenance
Removable pump
Disadvantages :
Difficult adjustment of weir opening
Low efficiency in waves
Low recovery in thin slicks (10%)
Not good with very high viscosity oil
Sensitive to debris

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weir Skimmer
Simple weir skimmer
Source: ExxonMobil

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weir Skimmer
Self-levelling weir

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weir Skimmer
Weir with integral screw auger
Source: ExxonMobil

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weir Skimmer
Source: ITOPF

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Skimming Operation

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sweep Arms

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sweep Arms

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weir Skimmer
Advancing weir skimmer
Source: ExxonMobil

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weir Skimmer
Source: ELASTEC

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weir Skimmer

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weir Boom
Weir boom skimmer
Source: ExxonMobil

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oleophilic Skimmers
Disc skimmers
Rope mop skimmers
Belt skimmers
Brush skimmers

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Disc Skimmer
Source: ITOPF
Advantages :
Good performance with light oil
High recovery efficiency
Not sensitive to debris
Simple maintenance
Disadvantages :
Low recovery rate
Limited viscosity range
Sensitive to sea grass

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Disc Skimmer
Source: ITOPF

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Drum skimmer
Drum skimmer
Source: ExxonMobil

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Skimmers

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Drum Skimmer
Grooved drum skimmer
Source: ExxonMobil

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Disc Skimmer
Disc skimmer
Source: ExxonMobil

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Disc Skimmer

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Disc Skimmer
Source: Korea Coast Guard

## Slide 28
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Disc Skimmer
Fabric-coated disc skimmer
Source: ExxonMobil

## Slide 29
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Rope Mop Skimmers
Advantages :
Low water content in recovered oil (10%)
Good performance in debris
Flexible ropes cover large area
Easy maintenance
Disadvantages :
Low recovery rate
Limited viscosity range
Difficult to deploy correctly

## Slide 30
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Rope Skimmer
Horizontal and vertical rope mop skimmer
Source: ExxonMobil
Source: ExxonMobil

## Slide 31
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Rope Skimmer
ZRV rope mop skimmer
Source: ExxonMobil

## Slide 32
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Belt Skimmer
Advantages :
High recovery rate
High recovery efficiency
Effective over wide viscosity range
Effective in high waves
Disadvantages :
Often very large
Require large vessel and heavy cranes for operation

## Slide 33
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sorbent lifting belt
Belt Skimmer
Source: ExxonMobil

## Slide 34
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Belt Skimmer
Submersion plane/belt skimmer
Source: ExxonMobil

## Slide 35
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Belt Skimmer
Source: DESMI

## Slide 36
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Brush Skimmer
Advantages :
High recovery efficiency
High recovery rate
Good performance in waves < 1 m
Easy maintenance
Disadvantages :
Large volume
Limited viscosity range

## Slide 37
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Brush Skimmer
Brush skimmer
Source: ExxonMobil

## Slide 38
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Brush Skimmer

## Slide 39
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Vacuum Skimmers
Advantages :
Lightweight and portable
Can handle more viscous oils
Disadvantages :
Limited suction length
Temporary storage needs to be close to suction head

## Slide 40
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Vacuum Skimmers

## Slide 41
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Vacuum Skimmers

## Slide 42
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Mechanical Skimmers
Advantages :
Can handle very heavy and emulsified oil
Disadvantages :
Often difficult to manoeuvre units
Works only in very heavy oil

## Slide 43
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Source: VIKOMA
Mechanical Skimmers

## Slide 44
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Water Jet Skimmer
Water jet skimmer
Source: ExxonMobil

## Slide 45
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Rotating Vane Skimmer
Rotating vane skimmer
Source: ExxonMobil

## Slide 46
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Paddle Belt Skimmer
Paddle belt skimmer
Source: ExxonMobil

## Slide 47
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Practical use of Skimmers
Oil must be in a state that allows for skimming to be effective.
Encounter rate is key.
Proportion of recovered oil to spilled oil is limited due to a variety of environmental and operational factors.
Recovery can become a bottleneck in the response if logistics of pumping and storage are not managed effectively.

## Slide 48
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Practical use of Skimmers
Need to consider complete logistics chain from:
  mobilization from storage or stockpile
  transport to staging area, dock, vessel or deployment area
  offloading from transport and transfer to site
  operating guidelines and running procedures
  fuel or power supply
  maintenance regimes
  decontamination prior to removal

## Slide 49
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Practical use of Skimmers
Need to consider operating procedures:
  deployment and recovery criteria (sea or swell limits)
  Number of personnel
  PPE
  H&S protocols during operations

## Slide 50
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Skimmer Overview
Source: ITOPF

## Slide 51
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Skimmer Overview

## Slide 52
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Pumps and Transfer Systems

## Slide 53
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Pumps
Key part of the recovery process.
Pumps are used to transfer recovered product from:
  skimmer to interim storage
  interim storage to transportation vessel/vehicle
  transportation vessel/vehicle to final storage/disposal facility.
May be on board the skimmer or separate.
Pump capacity effects the overall performance of a skimming system.

## Slide 54
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Transfer systems selected to suit quantities and types of liquids being moved.
Pumps lose efficiency with increase in viscosity.
Annular water injection, shortening hoses or increasing hose diameter can help improve pump performance.
Pumps

## Slide 55
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Pump Selection Matrix
Refer to ExxonMobil
Oil Spill Response Field Guide
Chapter 11
Source: ExxonMobil

## Slide 56
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Centrifugal Pump
pumping low viscosity fluids at high rates over short distances
supplying water, flooding shoreline

## Slide 57
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Lobe Pump
Source: ExxonMobil
pumping clean solid-free fluids
pumping heavier, viscous material
pumps against high back-pressures

## Slide 58
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Gear Pump
Source: ExxonMobil
similar to lobe pump
pumps very viscous fluids
can run dry without serious damage

## Slide 59
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Rotary Vane Pump
small, compact and easy to handle and repair
pumps low and high viscosity fluids

## Slide 60
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Flexible Impeller Pump
self-priming
can handle small suspended particulates
small, compact and easy to handle and repair in the field

## Slide 61
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Screw/Auger Pump
can pump highly viscous or semi-solid materials
Handles most debris

## Slide 62
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Progressive Cavity Pump
pumps various viscosities
can handle most debris
self-priming
does not emulsify oil/water

## Slide 63
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Reciprocating Pump
Can pump low to medium viscosity fluids at high pressures
strong self-priming capability and good suction lift

## Slide 64
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Diaphragm Pump
can run dry, self priming
good suction lift
air operated models are safe in explosive atmospheres

## Slide 65
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Peristaltic Pump
can run dry without damage
can pass most debris up to 25mm
self priming, good suction lift
can be reversed to clear blockages

## Slide 66
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Pumping Assistance
Annular injection flange
  aids pumping by reducing friction in discharge hose

## Slide 67
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Transfer Systems
Vacuum truck

## Slide 68
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Transfer Systems
Air conveyor
Source: ExxonMobil

## Slide 69
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Health and Safety
Keep hands/clothing away from moving parts.
Wear gloves.
Do not attempt to clear debris from a working skimmer.
Be aware of oil-covered surfaces.
Use caution around hydraulic hoses – safety glasses, hoses, whip checks.
Inspect equipment before and during use.

## Slide 70
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Summary
It is necessary to match a skimmer selection to conditions and to have access to a range of skimmer types to suit risks and oil weathering profile.
Examples:
Weir skimmers – mostly for open sea operations.
Oleophilic – many advantages in nearshore or onshore operations.
Vacuum skimmers – uncomplicated and lightweight.
Mechanical – normally only for heavy oil and debris.
Pumps are an essential part of the recovery process.

## Slide 71
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?