## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Assessment and Clean-up

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Objective
To understand the importance of shoreline assessment and the various clean-up techniques in order to reduce environmental damages.

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Assessment
In order to make decisions on shoreline treatment and response operations, management requires real-time data on oiling conditions.
This is the purpose of shoreline assessment and of a SCAT Team
(Shoreline Clean-up Assessment Technique)

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Assessment
Pre-spill planning phase
  Contingency plans
  Pre-SCAT data (such as mapping and segmentation)
  Resource maps

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Assessment
Response phase
  Implement contingency plans
  Review pre-SCAT data
  SCAT surveys
  Recommend shoreline protection and treatment

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Assessment Principles
Identify oiled and non-oiled areas
Identify location, amount and character of oil
Evaluate operational and logistical factors
Establish shoreline treatment priorities
Establish treatment standards
Propose treatment methods
Consider how proposed operations can prevent any additional damage

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Aerial Survey
Aerial reconnaissance using observations, photos, and video
Provides an overall picture of the situation in a short amount of time
Source: ITOPF

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Ground Survey
Provide more detailed information
May require a number of teams with differing skills
Can be done in addition to continuing aerial surveys

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Describe Coastal Conditions
Overview of characteristics of affected shore including load-bearing capacity
Operational activities take place in the backshore zone and this needs to be characterized.
Source : OSRL
Source : OSRL

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Mapping
Example of shoreline mapping and environ-mental sensitivity using ESI
Source: IPIECA/IMO/IOGP. Sensitivity Mapping for Oil Spill Response

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Describe Oiling Conditions
Surface oil distribution
Surface oil thickness
Oil character
Subsurface oil

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
SCAT Team
Made up of representatives for key stakeholders
Kept to a manageable size
Team members consult on oiling conditions for each segment and gain consensus to ensure an accurate unbiased view

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
SCAT Management
SCAT coordinator
Manages the team’s activities and coordinates with:
    Shoreline operations
    Documentation
    Logistics/Air ops

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
SCAT Management
  SCAT Logistics coordinator
  Takes care of the day-to-day field/office needs of the SCAT teams with respect to:
    Logistics – transportation, meals, water, supplies, field equipment
    Safety – PPE

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
SCAT Management
  SCAT Data manager
  Handles incoming field data, QA/QC and output products as required

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Stages of Shoreline Clean-up
Normally not an emergency – a project lasting weeks, months, years.
Stage 1. Removal of gross pollution and bulk oil
Stage 2. Removal of remaining stranded oil and oiled shoreline materials/debris
Stage 3. Final polishing/aesthetic treatment

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Overall objective of shoreline treatment is to
  remove the oil or
  to accelerate the natural recovery and
  avoid causing more damage by clean-up operations
Treatment Recommendations

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Treatment Recommendations
In order to make shoreline treatment recommendations:
Endpoints must be determined
Treatment methods are based on shoreline type and oil behaviour
Consider net environmental benefit when making recommendations

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Treatment Methods
  Natural recovery
  Physical methods
    Washing
    Removal and disposal
    In situ treatment
  Chemical and biological methods

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Natural Recovery
Estimate persistence and recovery
Will treatment accelerate recovery?
All treatment has an environmental effect – will the NEB be positive or negative?
What are the social/economic factors?
What are the safety issues?

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Physical Methods – Washing
Objective
This group of methods involves a variety of washing or flushing techniques that are used to remobilize and recover oil.

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Washing
  Washing
    Flooding
    Low pressure washing – cold
    Low pressure washing – warm/hot
    High pressure washing – cold
    High pressure washing – warm/hot
    Steam cleaning
    Sandblasting

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Washing
Technique | Pressure Range Bars PSI |  | Temperature Range °C °F | 
Flooding | < 1.5 | < 20 | Ambient sea water | 
Low-pressure: cold flushing | < 3 | < 50 | Ambient sea water | 
Low-pressure: warm/hot flushing | < 3 | < 50 | 30-100 | 90-210
High-pressure: cold flushing | 4-70 > 70 | 50-1000 > 1000 | Ambient sea water | 
High-pressure: warm/hot flushing | 4 – 70 | 50-1000 | 30-100 | 90-210
Steam cleaning | 4 – 70 | 50-1000 | > 100 | > 210
Sandblasting | ~ 4 | ~ 50 | N/A | 

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Technique | Objective | Optimum use
Flooding | Flood a site so that mobile oil is lifted and carried downslope to a collection area | Most shoreline type Light to medium oils
Low-pressure, cold wash | Wash or flush oils toward a collection area using ambient sea, lake or river water at low pressure | Impermeable shorelines and marsh Light to medium oils
Low-pressure, warm/hot wash | Wash or flush oils at low pressure, using heated water, toward a collection area | Impermeable shorelines Light to medium oils
High-pressure, cold wash | Wash or flush oils toward a collection area using ambient sea, lake or river water at high pressure | Impermeable shorelines medium to heavy oils
High-pressure, warm/hot wash | Wash or flush oils at high pressure, using heated water, toward a collection area | Impermeable shorelines medium to heavy oils
Steam cleaning | Remove stains or dislodge thin layers of viscous oil from hard surface | Impermeable man-made structures Stains or heavy, weathered oils

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Flooding
Source: OSRL

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Low Pressure Washing
Source: Exxon Mobil

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Low Pressure Washing
Source: OSRL
Source: Korea Coast Guard

## Slide 28
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
High Pressure Washing
Source: OSRL
Source: CEDRE

## Slide 29
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Physical methods  Removal
Objective
This group of physical methods involves removal of the oil or oiled material (sediments, debris, vegetation) from the shore zone for disposal.

## Slide 30
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Technique | Objective | Optimum use
Manual removal | Remove oil or oiled material (including oiled snow/ice) with manual labour and hand tool | Most shoreline types Small amounts of surface oil
Vacuum systems | Remove oil by suction from areas where it has pooled or collected in sumps | Light to medium, non-volatile, pooled or collected oil
Mechanical removal | Remove oil and oiled materials using mechanical equipment | Most fine to coarse-sediment beaches Large volumes of medium, heavy or solid oil
Vegetation cutting | Remove oiled stems to prevent remobilization of the oil or contact by animals and birds, or to accelerate the recovery of the plant. | Marshes, vegetated shorelines Where remobilization of oil will affect other resources.
Passive sorbents | Place sorbents in a fixed location(s) so that they pick up oil by contact | Any shoreline type Light to heavy, non-solid, non-volatile oils

## Slide 31
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Manual Removal
Source: OSRL
Source: CEDRE

## Slide 32
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Vacuum Systems
Source: OSRL
Source: Korea Coast Guard

## Slide 33
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Mechanical Removal
Important to consider bearing capacity of shoreline and other legal restrictions for heavy machinery

## Slide 34
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Mechanical Removal
Source: CEDRE
Source: OSRL

## Slide 35
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Vegetation Cutting
Source: CEDRE
Source: ITOPF

## Slide 36
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sorbents
Source: CEDRE
Source: CEDRE

## Slide 37
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Disposal
Waste management is a critical component to response operations
Segregation and minimization
Can cause a bottle-neck

## Slide 38
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Disposal
Oily waste and debris removal
Minimize sediment removal
Source: OSRL

## Slide 39
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Physical Methods – In Situ Treatment
Objective
This group of methods involves physical, on-site treatment techniques to promote or increase weathering and natural degradation.
    Mechanical tilling/Mixing
    Sediment reworking/Surf washing
    Burning

## Slide 40
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
In Situ – Tilling/Mixing
accelerate natural weathering penetrated or buried oil without sediment removal or waste generation
break up a surface oil cover before or after a resistant asphalt pavement forms
expose subsurface oil that might have been missed by the clean-up
release/recover oil by underwater agitation in a stream or during a rising tide without sediment removal

## Slide 41
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Mechanical Tilling
Source: Korea Coast Guard
Source: Korea Coast Guard

## Slide 42
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
In Situ – Sediment Surf Washing
move oiled sediments from one section of a beach to another in order to accelerate the natural removal of oil
oiled sediments are moved to an area where the physical action of waves is greater and is sustained for longer periods
  involves no sediment removal

## Slide 43
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sediment Reworking/Surf Washing
Source: CEDRE

## Slide 44
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Burning
Source: OSRL

## Slide 45
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Chemical/Biological Methods
Shoreline cleaners
Solidifiers
Bioremediation

## Slide 46
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Chemical/Biological Methods
Objective
Facilitate removal of the oil from the shore zone
Accelerate in situ weathering

## Slide 47
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Cleaning Agents
Oil is removed from solid surfaces
Contains surfactants, solvents and/or other additives
Requires appropriate PPE

## Slide 48
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Cleaning Agents
Source: ITOPF

## Slide 49
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Solidifiers
Solidifiers
Form a physical bond with the oil
Oil becomes solidified to a rubber like substance
Comes in various forms (powder, granule, semi-solid forms)
Must be contained and recovered

## Slide 50
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Bioremediation
Objective
accelerate the rate of degradation, typically by adding nutrients or oxygen to aid and increase natural bacteria – scope for effective use is limited
Rate will vary with
  Oil composition
  Surface area of oil exposed to bacteria
  Availability of nutrients
  Air/water temperature

## Slide 51
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Bioremediation
Source: CEDRE

## Slide 52
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Conclusion
SCAT teams are the “eyes” of Incident Command providing real-time data on oiling conditions
Shoreline treatment recommendations are made considering the net environmental benefit as well as logistical, operational and safety constraints

## Slide 53
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?