## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Management and Disposal

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Objectives
To understand the importance of waste management during an oil spill response;
To identify best practices in order to minimize the amount of waste generated during an oil spill.

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Issues
Planning
Types of waste
Temporary/intermediate storage
Transportation
Final disposal

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Worse Case Scenario: How Much Waste?
750 m3
3,750 m3
3,000 m3
750 m3 liquid waste for disposal
30,000 m3 solid waste for disposal
Impact the shoreline (mixed with 10x its volume of debris)
20% Recovered at Sea
Emulsified (80% water)
25% Evaporated
For 1,000 m3

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste management challenges can seriously affect the response efficiency

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Hierarchy
Response priority should be to minimize waste production as much as possible!
Reduce
Re-use
Recycle
Recover
Dispose

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Hierarchy
Source: IPIECA

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Management Planning
Should be carried out pre-spill and integrated into the contingency plan
Clean-up choices affect available disposal options
Minimize and segregate waste
Regulations, permits, approvals
  Must comply with local regulations

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Management Planning
Estimate volumes
Calculate resources required/available
Determine temporary storage sites and transportation methods
Minimize contamination of new sites
Determine final disposal sites
Cost-effective solutions

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Types of Waste
Liquid:
Oil
Oil/water mixture
Emulsion
Solid:
Oiled sediment
Oiled driftwood/seaweed
Oiled debris
Cleaning materials
  Sorbent materials
  PPE

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Temporary and Intermediate Storage
Significant quantities of waste are generated during clean-up operations
  Mainly by recovery at sea and shoreline clean-up
  Significantly less waste generated by using dispersants and in situ burning
If no storage is available, recovery operations will have to stop!
Important to think about the waste stream before beginning oil recovery operations

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Stream
Source: OSRL

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Temporary Storage
At sea:
Barges
Vessel tanks
Floating tanks
Onshore:
Skips
Portable tanks
Drums
Lined excavated (temporary) pits
Plastic bags

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
At-sea Storage

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
At-sea Storage

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Onshore Storage
Source: OSRL
Source: CEDRE

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Temporary Storage
Prevent secondary contamination
  Ensure storage is water/oil proof to avoid leakage
  Ensure site is suitable for temporary containers
    Flat with stable ground
    Easy access for heavy equipment
    Close to recovery sites
  Install liner under temporary containers
  Keep absorbent nearby in case of a small spill
  Ensure all vehicles used for waste transportation are decontaminated before leaving response sites

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Temporary Storage
Source: Korea Coast Guard

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Must be Separated!
By waste type
  Oil
  Solids (debris)
  Oil content
Facilitate storage, transport and final disposal
Ensure training and monitoring of working crews
Ensure appropriate containers are in place for all waste types at recovery sites
Source: ITOPF

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Think about Transfers!
Source: OSRL

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Transportation
Minimize waste before transportation
Minimize “double handling”
Prevent oiling of new areas
(secondary contamination)

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Waste Transportation
Source: OSRL
Source: OSRL

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Final Disposal
Re-use (after treatment)
Direct disposal  landfill
Stabilization - quick lime, road construction
Incineration
Land farming and composting

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Treatment and Disposal Methods
Source: IPIECA

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Summary of Options
Source: IPIECA

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Conclusion
Waste management can affect response effectiveness
Minimize – Segregate
Think about the waste stream
    Storage
    Transfer
    Transport

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?