## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Observation & Remote Sensing

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Objectives
To understand why observation is an integral/ essential element of spill response
To recognize what platforms may be available to you in the command centre
To understand the requirements for flight planning
To understand how to carry out visual observations
To understand how to quantify oil at sea

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Introduction
Observation is a key element in an effective response.
It enables us to:
  Assess the location and extent of the pollution
  Verify predictions of the movement and fate of oil at sea
  Interpret information to facilitate the deployment and control of operations at sea
  Identify threatened shorelines enabling protection of sites and the preparation of shoreline response.

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Initial Spill Assessment
Overflights should be a high priority in the initial stages of a response
The information we require for response strategy is:
  Confirm spill source/location and size
  Identify oil type and condition
  Identify local weather conditions and sea state
  Corroborate forecasted spill trajectory
  Identify potential areas at risk

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Initial Spill Assessment

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Spill Observation
The tools we have depend on local resources and availability but could include:
  Untrained observers
  Vessels, installations or ports-trained observers
  Aircraft with trained observers and portable equipment
  Dedicated remote sensing aircraft
  Unmanned surveillance platforms
  Satellite imagery
  Subsea sensors

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Untrained Observers
Untrained spotters
  Passing vessels
  Overflying aircraft
  Local fishermen and public
It may be the first indication you receive of a pollution incident
Their reports, especially location, size, colours and smell can be very useful
Use a proforma pollution report to debrief the observer

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Trained Observers
Trained observers will be used to observing and quantifying reports
They will provide more reliable depth with a higher confidence factor
They can compile observation reports and may provide photographic evidence
Their “height of eye” may be limited thus restricting their visual range

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Aircraft and Trained Observers
Often the most frequently available platforms
High-mounted wings offer good all-round visibility
Twin-engines are essential over water
Navigational aids, communications and endurance are important for long-range missions
Helicopters offer flexibility for near-shore missions especially for surveying intricate coastlines

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Aircraft and trained observers
Source: OSRL

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Trained Observers

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Remote Sensing Aircraft
Routinely used to detect, monitor and identify illegal marine discharges in a “patrolling” role
Can be used to respond to marine oil spills
Can be used to provide aerial command and control for at-sea operations
Fitted with highly-trained and experienced observers and specialist remote sensing equipment
Generally government owned/contracted

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Remote Sensing Aircraft

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Remote Sensing Aircraft
The most commonly employed sensors include:
  Side-looking Airborne Radar (SLAR)
  Downward-looking thermal Infra-Red (IR)
  Ultra-Violet (UV) imaging systems
Other systems include:
  Forward-Looking Infra-Red (FLIR)
  Microwave Radiometers (MWR)
  Laser Flurosensors (LF)
  Compact Airborne Spectrographic Imagers (CASI)

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Remote Sensing
Source: Maritime and Coastguard Agency

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Remote Sensing
Sensor | Coverage | Day | Night | Cloud cover, fog , haze, rain
SLAR | Wide area | Yes | Yes | Yes
Thermal IR | Narrow | Yes | Yes | No
UV | Narrow | Yes | No | No
FLIR | Narrow | Yes | No | No
MWIR | Wide Area | Yes | Yes | Possibly
LF | Narrow | Yes | Yes | No
CASI | Narrow | Yes | No | No
Combined SLAR and IR/UV systems have been used fairly widely during oil spills.

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Unmanned Aerial Systems
Relatively new but fast-growing market
Generally comprised of:
  Unmanned aerial platform with sensors
  Communications system
  Ground control station
  Sizes range from backpack portability to large systems requiring large vehicle transportation
Regulatory environment currently being developed

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Unmanned Aerial Systems
Aerostat – tethered ballons

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Unmanned Aerial Systems

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Unmanned Aerial Systems

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Satellite Sensors
Satellite-based sensors can detect oil on water
Sensors used include those operating in the visible and infra-red spectrum and Synthetic Aperture Radar (SAR)
SAR is not limited by daylight or clouds
SAR imagery can provide a lot of “false positives” and needs interpretation and on-scene corroboration

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Satellite Imagery
Advanced Synthetic Aperture Radar (ASAR) satellite image of the eastern Yellow sea 3.5 days after the HEBEI SPIRIT. Image provided by ESA.

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Imagery
The raw data captured by the sensors can result in huge volumes of electronic media
This media needs to be stored, analysed and distributed in a manner that can be used by decision-makers and planners
Linking the imagery with any modelled outputs is very useful
Timely analysis and distribution to the end users is critical if the imagery is to be effective

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Subsea Sensors
There are a range of oil detection sensors and oceanographic vehicles that can be used to track and detect oil in water.
Vehicles include:
  Autonomous underwater vessels (AUVs)
  Autonomous surface vehicles (ASVs)
  Remotely operated vehicles (ROVs)
  Manned surface vessels
  Typically these are employed by the scientific research communities, offshore industry and the military

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Subsea Sensors
The sensors include:
  Ultra-Violet (UV)
  Visible
  Thermal Infra-red (IR)
  Radar
  Fluorescence LIDAR
  The most frequent usage in oil spill response is with fluorometers to measure the efficiency of dispersant operations
  Other uses may include wreck survey and monitoring

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
AUV
Source: IPIECA JIP
AUV being deployed from NOAA research vessel near the Deepwater Horizon incident site

## Slide 28
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Aerial observation of oil at sea

## Slide 29
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Minimum Operating Requirements
The minimum requirements for aircraft are:
  Compliance with local and international aviation regulations (and associated certification)
  Supplemental Type Certificates (STC) that allow an operator to install and operate a given sensor
  Flight permissions
  Flight plan
  Good downward visibility
  Slow speed capability

## Slide 30
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Minimum Operating Requirements
The minimum requirements for aircraft (contd)
  Effective communications with vessels and ground
  Trained and equipped personnel for operating the platform and sensors and /or making manual spill observations
  Sensor suite incorporating a minimum of digital camera/video with positional information and data link to control centre
  High accuracy dynamic positioning system integrated with sensor suite

## Slide 31
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Weather conditions such as fog, mist, low cloud, snow and heavy rain can affect surveillance
High winds may mean flying is impractical
A flight plan should be prepared in advance, agreed with the pilot and the command centre taking into account visibility, altitude, direction of sun, flight duration, fuel availability and communications
Flights should be planned from start to finish allowing sufficient light for observation
Flight Planning

## Slide 32
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Observations should be recorded on a proforma observation log with photographs and video linked to GPS.
Fast shutter speeds (1/500th second) are recommended.
Haze and light reflection can affect visibility. Positioning the sun behind the observer is easiest.
Polarizing sunglasses can assist under certain light conditions.
Flight Planning

## Slide 33
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Incident Management
Command Function
Planning Function
Logistics
Function
Finance Function
Operations Function
Data
Observation

## Slide 34
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Visual Quantifying Oil at Sea

## Slide 35
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Visual Quantifying Oil Volumes
Accurate assessment of quantity is not possible due to difficulties in assessing the thickness and coverage of the oil.
The Bonn Agreement Oil Appearance Code describes the relation between the appearance, thickness and volume of floating oil.

## Slide 36
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Code | Appearance | Approximate thickness (μm) | Litres per km²
1 | Sheen (silvery/grey) | 0.04 – 0.30 | 40 - 300
2 | Rainbow | 0.3 – 5.0 | 300 – 5,000
3 | Metallic | 5.0 – 50 | 5,000 – 50,000
4 | Discontinuous True Oil Colour | 50 – 200 | 50,000 – 200,000
5 | Continuous True Oil Colour | 200 + | 200,000 +
Bonn Agreement Oil Appearance Code
Estimation of range (upper and lower figures)

## Slide 37
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Code 1 – Sheen/Code 2  Rainbow
Source: Bonn
CODE 1 ‘SHEEN’ + CODE 2 ‘RAINBOW’

## Slide 38
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Code 3 - Metallic
Source: Bonn
Code 3 ‘Metallic’ appears as a homogeneous colour. It acts like a ‘mirror’ that is dependent on light and sky conditions. When the sky is ‘blue’ – the colour blue will be observed.

## Slide 39
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Sheen, Rainbow and Metallic
Source: ITOPF

## Slide 40
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Discontinuous True Colour
Source: Bonn
50 m to 200 m
Code 4 – Discontinuous true colour  consists of small areas, or patches, of Code 5, Continuous true colour in a background of Code 3, Metallic.

## Slide 41
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Source: Bonn
Discontinuous True Colour

## Slide 42
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Continuous True Colour
Source: Bonn
CODE 5
200 m +

## Slide 43
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Continuous True Colour
Source: Bonn
200 m +
CODE 5  CTC

## Slide 44
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Continuous True Colour
Source: Bonn

## Slide 45
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Source: Bonn
HEAVY FUEL OIL
Continuous True Colour

## Slide 46
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Source: Bonn
Water in Oil Emulsification
Emulsified oil can range in colour from dark brown to almost red or tan and typically has a “thickened” or “pudding-like” consistency compared to freshly spilled oil.
The incorporation of up to 80% water into the oil will cause the apparent volume of a given quantity of oil to increase four times.

## Slide 47
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Emulsified crude oil accumulated against a salt marsh by an onshore wind. The wedge of oil formed in this way can be several cm thick.
Emulsified Oil
Source: NOAA

## Slide 48
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Source: Bonn
Oil Pancakes
Isolated patches of roughly circular shaped oil that range in size from around a metre to hundreds of metres in diameter become pancakes. Sheen may or may not be present.

## Slide 49
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Source: Bonn
Tar balls
Discrete, and usually pliable, globules of weathered oil, ranging from oil to highly emulsified with varying amount of debris and/or sediment.

## Slide 50
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Source: Bonn
Windrows
Streaks of oil that line up in the direction of the wind.
The lines are roughly parallel to the wind direction, and the windier it is, the further apart the lines tend to form very early in a spill where the wind is 6 knots or greater.

## Slide 51
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Cloud shadow
Source: NOAA
Oil Look Alike’ Phenomena

## Slide 52
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Underwater growth of kelp resembling patches of black oil.
Altitude 250 m.
Source: NOAA
Oil ‘Look Alike’ Phenomena

## Slide 53
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oil Look Alike’ Phenomena
Jellyfish from 15 m taken by helicopter.
Source: NOAA

## Slide 54
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oil Look Alike’ Phenomena
Algae blooms
Source: NOAA

## Slide 55
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?