## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Containment, Recovery and Salvage Considerations

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Objective
To provide a short introduction to containment
To consider how containment may be used as an operational tactic
To provide a short introduction to recovery
To consider how recovery may be used as an operational tactic
To provide a short introduction to salvage operations and some general salvage techniques
To consider some Place of Refuge considerations and how they are applied within the incident response
To consider how salvage operations can be integrated within the Incident Command

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Containment

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Containment
Containment objectives include:
  To prevent the initial discharge from spreading, if used promptly
  To prevent both continuous and further discharges from spreading
  To corral and thicken oil for recovery or burning
  To protect sensitive resources and environments
  To deflect a spreading slick away from sensitive resources and habitats
  To deflect a spreading slick to areas from which it can be more easily recovered

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Containment

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Containment
  Each objective requires careful planning, selection and deployment of resources
  Close cooperation between Operations, Planning and Logistics functions
Command Function
Planning Function
Logistics
Function
Finance Function
Operations Function
Response
Planning
Booming
Operations
At-Sea Recovery
Near-shore Containment
Resource Deployment

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Selection
Different types of boom are designed for specific operating environments and purposes:
  Rapid deployment
    In ports, marinas, offshore installations
  Calm and sheltered waters
    Ports, etc.
  Shoreline sealing
    Tidal conditions
  In situ burning
  Open water

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Selection
The selection of boom types and sizes will be dependent on:
  The planned deployment purpose
  The proposed location
    Calm water, low current, open water
  The deployment platform
The following factors need to be considered:
  The environmental conditions
    Wind, waves, tide/current
  The buoyancy/weight ratio of the selected boom

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Types
Many different types of booms but generally they fall into four main groups:
  Curtain-type boom
    Generally have distinct buoyancy chambers and a skirt
    Include solid flotation, air-inflatable and self-inflatable
  Fence boom
    Includes standard fence and external tension member booms
  Shore-seal boom
  Fire-proof boom (refer to module on ISB)

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Types
Source: ExxonMobil
Source : ITOPF
Source : ITOPF

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Alternative Barriers
There are a number of other boom types that do not fall into the main categories described:
  Pneumatic barriers
    Employing a screen of air bubbles released below the water surface
  Net booms
    Designed primarily to contain viscous oils
  Makeshift/improvised barriers
    Created locally from readily available materials
    Consider what material and designs may be available locally during the planning process

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Alternative Barriers
Source : ITOPF
Oyster shells
Straw bales

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Selection Criteria
 | Calm Water | Calm Water Current | Protected Water | Open Water | Open Rough Water
Wave Height (m) | < 0.3 | < 0.3 | 0 – 1.0 | 0 – 2.0 | > 2
Conditions | Small short non-breaking waves | Currents of 0.4 m/s or greater | Small waves and some white caps | Moderate waves and frequent white caps | Large waves, foam crests and some spray
Suitable boom type or group | Curtain Fence | Curtain with freeboard of 50% of boom height Fence | Curtain Fence | Curtain Fence with external tension support | Curtain
Boom Height (mm) | 150 - 600 | 200 - 600 | 450 – 1,100 | 900 – 2,300 | 1,500+
Buoyancy-to-weight ratio | 3:1 | 4:1 | 4:1 | 8:1 | 8:1
Minimum tensile strength of boom (Newtons) | 6,800 | 23,000 | 23,000 | 45,000 | 45,000+

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Limitations and Failures
Booms may fail operationally in one of five main modes:
  Entrainment
  Drainage
  Splash over
  Submergence
  Planning failure
These failures are covered in greater detail in the Level 1 course
Containment systems typically have a relatively low oil-encounter rate and their operation in rougher seas may be ineffective and raise serious safety concerns

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Limitations and Failures
Boom may also suffer structural failure when placed under stress. This is normally associated with boom deployment outside their design limits.
Containment operations, like all other tactical options, must be technically reasonable, preferably planned in advance, and conducted in a safe manner within the design limits of the equipment.

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Boom Limitations and Failures
Source: OSRL
Source: ITOPF
Source: ITOPF

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Containing at-Source
Containing a spill from a fixed source such as a vessel alongside a jetty or aground requires careful planning
The advantages/disadvantages of this option must be considered:
  Do the environmental advantages outweigh any safety considerations?
  The type of oil being released and the sensitivity are the key factors in this decision

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Containment
This table provides some general planning guidance on boom lengths for different protection applications:
Application | Quantity of Boom
Encircling a stricken vessel | 3 x ship’s length
Containment of an operational spill from a vessel at a terminal | 1.5 x ship’s length plus distance from bow and stern to shore
Protection of an entrance to an estuary, stream, river, etc. | 34 x width of the body of water
General booming in bays and harbours | 1.5+ current in knots x width of water body

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Tactical Considerations  Booms
In summary:
Is it technically reasonable?
Does it meet our NEBA criteria and considerations?
Is it allowed under our regulations?
Do we have the resources?
Can we monitor the effectiveness?
Note: Risk assessment of current and expected conditions in addition to NEBA

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Protection and Containment Plans
Protection Plan
  Things to consider
    What sites do you want to protect?
    How much boom is available?
    Do you have sufficient ancillaries such as anchors, ropes, buoys?
    Do logistical considerations allow for boom deployment to sites?
    Does time permit boom deployment prior to oil reaching site?
    If limited boom is available, boom should be deployed to sites as prioritized.

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Protection and Containment Plans
Containment Plan
  Things to consider:
    Type of oil
    Can it be contained?
    Trajectory – Where is it headed?
    Locations where containment is feasible
    Shorelines
    Can booms be deployed?
Places to anchor boom
How much boom is needed to contain oil in location
Is sufficient boom available?
Are boats available to deploy boom?
Are personnel available to deploy and maintain boom?

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Protection and Containment Plans
Containment Plan
  Ongoing plan adjustment
    Monitor path of oil to determine where changes in strategy are necessary
    Use modelling trajectories and observation throughout response
    When window of opportunity for alternative response mechanisms (dispersants, ISB, bioremediation) has passed, have a back-up plan for containment and recovery
    When oil comes ashore, implement shoreline clean-up plan
    Meet regularly to monitor status of clean-up operations
    If not enough personnel and equipment are available, prioritize strategies for response operations

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
On Completion
Consideration should be given to:
  Determining when the boom should be removed or redeployed elsewhere
  What resources are required to recover the boom
  How and where the boom will be cleaned before being redeployed or returned
  The organization of the temporary cleaning area, including any permits and provision of personnel and materials
  The recovery, capture and disposal of any waste

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Recovery

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Recovery Operations
Recovery objectives include:
  Physically recovering the oil from the water surface
  Minimizing any further damage to marine resources and the environment
  Reducing the amount of oil that may impact the shoreline
  Recovering floating oil from shoreline clean-up operations

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Recovery Operations
  Each objective requires careful planning, selection and deployment of resources
  Close cooperation between Operations, Planning and Logistics functions
Command Function
Planning Function
Logistics
Function
Finance Function
Operations Function
Response
Planning
At-Sea Recovery
Near-Sea Recovery
Resource Deployment

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Tactical Considerations  Recovery
In summary:
Is it technically reasonable?
Does it meet our NEBA criteria and considerations?
Is it allowed under our regulations?
Do we have the resources?
Can we monitor the effectiveness?
Note: Risk assessment of current and expected conditions in addition to NEBA

## Slide 28
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Recovery Devices
Different types and sizes of recovery devices are designed for specific operating environments and different types of oil:
  Light to medium oils in sheltered waters
    Ports, marinas, rivers and estuaries
  Light to medium oils in open waters
    Open waters, offshore
  Heavy oils in sheltered waters
    In ports, rivers and estuaries
  Heavy oils in open waters
    Open waters, offshore

## Slide 29
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Recovery Devices
Source: ELASTEC

## Slide 30
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Recovery Devices
Diverse range of devices available
Generally fall into one of four main categories, although some incorporate dual features:
  Weir devices
  Adhesion devices
  Induction devices
  Devices using other principles

## Slide 31
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Recovery Devices
On water single- or multi-vessel operations
Generally a low height of eye so need guidance from above or specialized location devices
Usually limited to daylight hour operations so need to be in position before first light to maximize recovery time
Transit speeds, including course changes and 180⁰ reversals with booms deployed is low

## Slide 32
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Recovery Devices
On water single- or multi-vessel recovery operations
Source : ITOPF

## Slide 33
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Recovery Devices
A large proportion of water may be collected
Operations at night may be possible utilizing IR cameras or oil-sensing radar
The use of local resources and knowledge is highly recommended
Local water users know the local conditions and can be a very valuable resource

## Slide 34
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Recovery Devices
In addition to containment devices they require pumps to move/push the recovered oil to the temporary storage area
This will require a set of support equipment with the correct connections and couplings
It is important to reduce the back-pressure in the discharge hose
Offshore recovery devices are heavy and will require lifting equipment to deploy and recover

## Slide 35
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Subsea Recovery Devices
In shallow waters these can include suction pumps, airlift dredge systems or oleophillic sorbents.
Sunken vessels can be “hot-tapped” to gain access through the vessel’s hull. These systems can be diver- or ROV-operated, generally by salvors.
Deep-sea release containment involves the use of a “capping stack” to gain control of a blown-out well. A number of these devices are available world-wide.

## Slide 36
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Safety
There are a number of safety concerns that should be addressed by risk assessment
These include:
  Type of oil and associated hazards
  Working near water
  Working on decks covered with oil
  Weather conditions and movement of vessel
An operational plan must be provided for each vessel detailing its specific operations, including risk assessments

## Slide 37
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Temporary Storage
Temporary storage is critical for ongoing operations
This may consist of:
  Vessel tanks
  Barges
  Towable tanks
When using chartered vessels not constructed as Tankers special considerations need to be given to storing and handling recovered oil

## Slide 38
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Temporary Storage
Source:CEDRE
Source:CEDRE

## Slide 39
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Temporary Storage
  When providing temporary storage ensure there will be sufficient capacity for ongoing operations
  Consider how the recovered oil will be discharged from the storage tank
  Consider the use of heating coils for viscous or cold recovered oil
  Consider the use of oily water separators to reduce the amount of recovered water
  Discuss a possible dispensation from the MARPOL regulations with the Administration in respect of decanting operations

## Slide 40
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
On Completion
Consideration should be given to:
  How and where the vessels will be cleaned before being re-deployed or taken off charter
  The organisation of the temporary cleaning area, including:
    any permits
    booming and containment
    provision of personnel and materials
    provision of lifting equipment or small craft
  The recovery, capture and disposal of any waste

## Slide 41
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Salvage Considerations

## Slide 42
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Introduction
There are a number of reasons why oil can be lost from a vessel:
  Collision
  Grounding
  Striking a wreck or other obstacle
  Fire and/or explosion
  Machinery or structural failure
  Storm or ice damage
  Flooding
  Sabotage

## Slide 43
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Incidents

## Slide 44
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Introduction
The Master, as representative of the vessel, and cargo owners will take immediate action to ensure the:
  Safety of the crew
  The preservation of the ship
  The preservation of the cargo
  Stopping or limiting of the cargo loss
The Master may require specialist help for the salvage of the vessel

## Slide 45
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Introduction
Salvage assistance will generally be arranged, on commercial terms, with a professional salvage company
In respect of tankers the salvage company is rewarded for operations, including preventative measures, that prevent or minimize pollution damage
The salvor’s primary aim will be the successful completion of his assignment in a timely fashion

## Slide 46
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Introduction
An Administration, under its national law or under the Intervention Convention, may take powers to intervene when their waters or coastline are under threat from pollution
The salvage operation will be conducted between the owner/operator and salvor with both parties complying with the requirements of the Administration
It is important that there is full cooperation between all parties

## Slide 47
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Emergency Response
Emergency response and follow-up actions:
  Lightering
    Cargo or bunker transfer
  Towage
    Shelter or re-floating
  Salvage
    Re-floating or wreck removal
  Pollution combating
  Protection of local population

## Slide 48
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Response
Is intervention at sea the best option?
Balance the opportunity to prevent the oil leaving the vessel against the possible consequences:
  Risk to human health and safety
  Damage to vessel and cargo
  Damage to the environment
Administrations are urged not to unreasonably deny access to sheltered waters

## Slide 49
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Response
Is it possible?
If intervention at sea is desirable:
  Can it be done?
  Is the expertise available?
  Is the equipment available?
Your contingency planning should address these questions

## Slide 50
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Incident Command
Within the Command Function the salvage response should focus on:
  Notifying the relevant authorities
  Establishing the facts and assessing the damage potential of the incident
  Establishing and maintaining contact with all parties concerned
    Shipowner, cargo owner, salvors, insurance interests, classification society, Flag State

## Slide 51
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Incident Command
  Decide whether salvage activities being undertaken by the owner are adequate
  Decide what additional steps the Command Function can take to facilitate salvage and prevent pollution

## Slide 52
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Incident Command
  Organize the prompt availability of specialist assistance and salvage materials
      This may include assistance with Customs, Immigration or logistical facilitation
      This may include the provision of government equipment, access to government stockpiles or response assistance

## Slide 53
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Incident Command
  Review and approve, as appropriate, the salvage plan including the appropriate risk assessments for the proposed operations
  Consider “Places of refuge” to facilitate the salvage operations
  Impose and enforce Temporary Exclusion Zones and Temporary Danger Areas
  Ensure close cooperation between the salvage operation and the Operations and Planning functions

## Slide 54
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Salvage Operations
  Salvage is a highly technical and complex process which, where possible, is best conducted by professional salvors
  These salvors may need further specialist expertise such as from the offshore industry to respond to pipeline and offshore installations
  In the same manner that Search and Rescue (SAR) operations may be conducted alongside the incident response, both SAR and salvage operations are critical components of the overall response

## Slide 55
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Salvage Operations

## Slide 56
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Salvage Operations
  Some common salvage methods are:
    Lightering
        The transfer of cargo or bunkers to a suitable vessel or ashore in order to lighten the vessel
        May also include the internal transfer of cargo to minimize or reduce the risk of fire, explosion or pollution
    Air Lift
        Displacement of water by air pressure, especially where tanks have been opened to the sea.
        All tank opening needs to be sealed to withstand the pressure increase
        If possible move cargo or bunkers to minimize any pollution

## Slide 57
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Salvage Operations
  Some common salvage methods are:
  Tidal lift and heaving
    This method uses the power of the rising tide to assist in re-floating but may require heavy “beach gear” consisting of anchors, wires, etc.
  Towing
    Relies on the pulling power of salvage vessels or tugs
    This requires appropriate towing lines and securing points on the casualty
    SOLAS requires tankers to be fitted with appropriate emergency towing facilities
    Local tidal knowledge is very important to ensure that the pulling forces are applied in the most effective direction

## Slide 58
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Salvage Operations
  Some common salvage methods are:
    Re-floating or breaking out stranded vessels
      Re-floating relies on overcoming the downward force exerted by the stranded vessel on the sea bed
      This could be by reducing the weight of the stranded vessel by lightering
      This could be by increasing the floating force by using pontoons, barges or air bags
      This could be by excavating the ground beneath the stranded vessel

## Slide 59
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Salvage Operations
  Some common salvage methods are:
    Capping and containment of offshore pipework
      Specialized capping devices installed using specialized subsea operations vessels and ROVs

## Slide 60
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Salvage Equipment
  In every case specialized expertise and knowledge will be required
  This may be a combination of salvage experience and knowledge of the local conditions
  Often specialized equipment needs to be brought to the site
  This can take time during which the stranded vessel will be exposed to the sea and weather
  In some cases the vessel may be deliberately stranded awaiting the equipment

## Slide 61
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Salvage Process
  Salvors will carry out inspections, including diving inspections, to ascertain the current condition of the vessel
  Damage control measures may be put in place to prevent any further deterioration or movement
  The salvage plan will be drawn up in consultation with naval architects and the shipowners or operators
  Normally this salvage plan will be discussed and agreed with the Administration and Incident Command

## Slide 62
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Response – Evaluation
Place an evaluation team on board:
  Experienced personnel equipped with appropriate personal protective equipment
Ascertain full status of the vessel
    Cargo, bunkers and disposition
    equipment and facilities on board
    operational status of machinery, etc.
Carry out risk assessment

## Slide 63
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Place of Refuge Considerations
The assessment process
Likelihood/Consequence matrix
Risk register
The resources and expertise available
Procedures for decision-making
Procedures for international coordination
Financial guarantee and liability procedures

## Slide 64
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Decision-making process Source: REMPEC SAFEMED Project 2005/109-573
Place of Refuge

## Slide 65
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Likelihood/Consequence Matrix
Likelihood | Consequence |  |  |  | 
 | Insignificant | Minor | Moderate | Major | Catastrophic
Almost Certain (>90% chance) | High | High | Extreme | Extreme | Extreme
Likely (50% ~ 90% chance) | Moderate | High | High | Extreme | Extreme
Moderate (10% ~ 50% chance) | Low | Moderate | High | Extreme | Extreme
Unlikely (3% ~ 10% chance) | Low | Low | Moderate | High | Extreme
Rare (<3% chance) | Low | Low | Moderate | High | High
Example

## Slide 66
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Risk Register  Example
ID | Risk | Consequence | Consequence
 |  | Remain in Situ | Place of Refuge
1 | Crew Safety | High | Low
2 | Responder/Salvor Safety | High | Low
3 | Public Safety | Low | Medium
4 | Pollution – Cargo | High | Low
5 | Pollution - Bunkers | High | Medium
6 | Navigational Safety | Low | Low
7 | ……………….. |  | 
8 | ……………….. |  | 

## Slide 67
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Incident Management
Command Function
Planning Function
Logistics
Function
Finance Function
Operations Function
Response
Planning
Salvage
Operations

## Slide 68
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Incident Command
  Let us discuss where salvage operations fit into IMS
  Consider this:
    If salvage operations are being conducted within the Incident Command then does participation within the Operations and Planning Functions seem appropriate?
    If salvage operations are being conducted outside of the Incident Command then consider liaison into the Command Function and participation within the Planning Function
    Consider the Coordinated Command model
  How will you integrate salvage operations?

## Slide 69
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?