## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Lesson 3.6 Impacts of Oil Spills

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Objective
To recognize potential impacts of oil spills.
To use this information to elaborate the overall response strategy.

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts of Oil Spills
Oil spills can adversely impact:
  Health and safety due to oil toxicity
  Social and economic activities
  Marine and coastal environment
Impacts can be from:
  Interference with activities
  Oil toxicity
  Smothering

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oil Toxicity
Will depend on:
  Oil type and concentration
  Exposure duration
  Sensitivity of organisms
Toxic components:
  Polycyclic Aromatic Hydrocarbons (PAHs)
  Light fractions
    BETX (Benzene, Ethylene, Toluene, Xylene)
  Heavy metals

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Oil Toxicity
Generally:
  Light oil: effects are from oil toxicity
  Heavy oil: effects are from smothering of organisms

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Acute Effects
Heavy and medium crude oil
  Smothering of organism
  Asphyxia
Light components
  Ingestion or inhalation
  Contamination of flesh

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Chronic Effects
Physiological problems
  Decrease productivity
  Slower growth
  Decrease olfactive capacity (marine mammals)
Behavioural disruption
  Slower reaction time
  Feeding problems
  Reproductive problems
Bioaccumulation/depuration

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts of Oil
Important to differentiate between impacts on individuals and those on population
  A few individuals may suffer severe adverse effects with no impacts to overall population.
Impacts from oil have been studied since the first major shipping incidents.
Generally, short term impacts with moderate to low long term impacts.

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Factors Affecting the Impact of Oil
Type of oil and degree of weathering
Biological characteristics of the area
Geographic location
Degree of oiling
Oceanographic and meteorological conditions
Season
Choice of response strategy and effectiveness of response

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Costs of Incidents
In addition to the impacts of incidents from a socio-economic and environmental perspective consider the costs of an incident:
  BRAER (1993): GBP 51 M*
  ERIKA (1999): Eur 129.7 M*
  PRESTIGE (2002): Eur 121.8 M*
  DEEPWATER HORIZON (2010): US$ 40 B (estimate)**

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Social and Economic Activities

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Social and Economic Activities
Presence of oil will interfere with normal activities
Can cause financial losses and loss of enjoyment
All coastal activities can be impacted

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on tourism:
  Important for many coastal communities
  Direct oil impacts on beaches and coastal structures can lead to closures
  Potentially fewer clients for restaurants, hotels, water parks, etc.
  Positive financial impacts from oil spill workers
  Impacts are generally short-lived and activities resume following clean-up, however there can be significant image damage that may persist
Social and Economic Activities

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Social and Economic Activities
Impacts on water intakes:
  Many industries need water to function properly:
    Power and desalination plants
    Fish plant
    Aquarium, pools, etc.
  Oil in a water intake can lead to contamination of water supply, malfunctions, etc.
  Can have serious implications, e.g. power plant
  Important to protect these areas to avoid contamination

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on ports and marina:
  Ports are the entrance or exit for many essential goods and trade
  Ports and marinas can be affected by:
    Navigation channels closed or restricted
    Contamination of structures such as wharf, jetties, etc.
    Contamination of vessels
    Closure or limited access due to response operations (booms)
  Cleaning of vessels is often required
  Contaminated structures can be difficult to clean
Social and Economic Activities

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Social and Economic Activities
Impacts on coastal communities:
  In many parts of the world, populations live near or on the coast
  Exposure to oil vapours can cause breathing difficulties, headaches and nausea
  Usually, vapours are present at the beginning of a spill and the impact is likely to be short-lived
  Daily activities can be impacted by the presence of oil and by response operations

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Social and Economic Activities
Impacts on archaeological sites and coastal artefacts:
  Many archaeological sites and associated artefacts are found in coastal areas.
  These areas can be contaminated by direct contact with oil.
  These areas are very sensitive and clean-up methods must be adapted to preserve these sites.
  Archaeologists are required to identify these areas and to provide recommendations for clean-up

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Social and Economic Activities

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Marine Environment

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Marine Environment
Plankton
  Very sensitive to oil
  Affected by dispersed oil (naturally or chemically)
  Mortality is compensated by over-production of young life stage and recruitment from non-affected area
  Significant decline has not been observed following an oil spill

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Marine Environment
Fish
  Juveniles susceptible to oil exposure
  Adults more resilient, free-swimming fish will avoid oil
  Mortality associated with localized conditions
    Dispersed oil (naturally or chemically)
    Shallow waters, light oil
  Depuration processes
  Generally low impacts on fish population

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Marine Environment
Marine mammals
  Whales, dolphins, seals, otters, manatees, etc.
  Species surfacing to breath can be exposed to floating oil
  Irritation to airways, eyes has been reported
  Generally no mortalities but may be exceptions
  Species using the shoreline such as seals and otters can suffer from oil exposure especially if their haul-out is contaminated

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Marine Environment
Marine mammals
  Furry animals can suffer from hypothermia if the fur is oiled
  Generally, impacts are mild with skin irritations and disruption the most reported
  Mortality is usually rare following an oil spill

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Marine Environment
Sea turtles
  All species are endangered
  They are vulnerable to oil particularly during nesting season and in shallow waters
  They use sand beaches for nesting and to lay eggs so clean-up of these areas during nesting season will be high priority
  Adults can suffer irritation and inflammation of membranes
  It is possible to clean sea turtles

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Marine Environment
Seabirds, wildfowl and waders
  Are vulnerable to floating oil
  Large numbers can die from contact with floating oil at sea or on shorelines
  Oil disrupts the feathers, affecting insulation properties which results in hypothermia
  Birds will also ingest oil as they attempt to clean their feathers
  Exhaustion resulting from smothering, particularly following exposure to viscous oils, is a commonly observed effect

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Marine Environment
Seabirds, wildfowl and waders
  Contamination of habitat especially during nesting season can cause significant impacts
  Oiled birds can be cleaned and rehabilitated but depending on species it may be that only a small fraction will survive
  Short and long-term damage is possible for individuals and population

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Marine Environment
Seabirds, wildfowl and waders

## Slide 28
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Marine Environment
Corals
  Highly sensitive organisms
  Long recovery time if exposed to oil
  Can be exposed to dispersed oil especially near shore with high energy breaking waves
  Exposed coral reef can be affected by floating oil
  High priority areas for protection

## Slide 29
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on coastal environment

## Slide 30
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Coastal Environment
Shorelines
  Shorelines are almost always impacted during an oil spill
  Degree of sensitivity to oil is very variable between shoreline types
  Impact is related to oil persistence and biological activity

## Slide 31
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Coastal Environment
Mangroves
  Highly sensitive to oil
  Trees suffer from asphyxia from oil coating of roots and pores
  Clean-up is extremely difficult and recovery can take decades

## Slide 32
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Mangroves
Impacts on Coastal Environment

## Slide 33
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Coastal Environment
Marshes
  High biological importance
  Plants are relatively resistant to oiling
    Will depend on growth cycle
  Long-term impacts due to oil penetration in the substrate affecting the root system
  Penetration is generally caused by trampling or use of mechanical equipment
  Needs to be considered on a case-by-case basis

## Slide 34
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Coastal Environment
Marshes

## Slide 35
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Coastal Environment
Mud flats
  Used by many vertebrate and invertebrate species
  Low energy shoreline
  Long-term impacts are generally caused by oil penetration in sediments caused by trampling or oil penetration through worm burrows

## Slide 36
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Coastal Environment
Mud flats

## Slide 37
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Coastal Environment
Rocky shorelines
  Less biologically active
  Usually, they are colonized by algae or small invertebrates
  Recolonization can be rapid following an oil spill
  Short-term impacts are typical for these shorelines

## Slide 38
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Coastal Environment
Rocky shoreline

## Slide 39
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Coastal Environment
Sandy shorelines
  Less biologically active
  Short-term impacts are typical for these shorelines
  Potential for oil burial due to sand movement
  Potential for oil and sand interaction in the inter-tidal zone leading to sunken oil

## Slide 40
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Coastal Environment
Sandy shoreline

## Slide 41
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Marine Environment
Post-spill studies
  Various studies can be undertaken to evaluate environmental damage
    Chemical analysis, population inventories, etc.
  Should have clear objectives and achievable goals
  Importance of pre-spill background data
Restoration measures can be identified and implemented in some cases

## Slide 42
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts Affecting Operational Response
The impacts of oil spills on the various activities and environments can affect the operational response
  Public/media attention to operational activities especially in areas of high population density
  Access restrictions due to the impact’s proximity to sensitivities such as cultural sites, private property, etc.
  Seasonal restrictions due to wildlife nesting, etc.
  Prioritization of operational activities

## Slide 43
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Fisheries

## Slide 44
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Fisheries
Fisheries and mariculture are important economic and subsistence activities.
Fisheries can be affected by oil because of:
  Smothering
  Toxicity
  Tainting (oil taste in flesh)
  Business disruption.

## Slide 45
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Fisheries
Mariculture is particularly vulnerable
  Animals cannot escape
  Oiling of equipment
  Some species will eliminate oil over time (depuration)
Free-swimming fish are rarely affected unless they are exposed to dispersed oil

## Slide 46
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Fisheries
Many concerns when fisheries are affected:
  Public health concerns
    Toxic compounds (PAHs) in flesh
    Many international guidelines
  Market confidence
    Sales might be affected even if fish are not contaminated by oil
  Fisheries closure
    Often implemented during an oil spill

## Slide 47
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Fisheries
Management strategies:
  Organoleptic testing
    Detect taste and odours of oil in flesh
  Sampling and chemical analysis
    Detection of toxic compounds in flesh
    Compare results with public health guidelines
  Marketing campaign to restore confidence

## Slide 48
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Impacts on Fisheries

## Slide 49
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Points to Remember
Oil spills interfere with coastal activities
Effects on marine life are caused by:
  physical contamination and smothering
  tainting as a result of the smothering and toxic effects
Health of populations is more important than individuals

## Slide 50
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Points to Remember
Recovery time is highly variable.
Clean-up techniques can cause further damages.
Identify and prioritize areas to be protected at contingency planning stage.

## Slide 51
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?