## Slide 1
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Lesson 3.7 Oil Spill Response Options

## Slide 2
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Objective
Provide an overview of oil spill response options;
Provide information on advantages and disadvantages of each option; and
Provide a methodology to select the appropriate response options.

## Slide 3
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Response Objective
The overall objective of oil spill response is to minimize impacts on:
  Biological resources
  Economic activities
  Human use of shoreline
A limited number of response options are available to achieve this objective
No universal option!
Oil type, weather conditions and oil trajectory will affect choices

## Slide 4
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Response Options
The following response options are available to responders:
  Aerial surveillance, tracking and forecasting
  Protection of sensitive resources
  Containment and recovery
  Dispersants
  In situ burning
  Shoreline clean-up

## Slide 5
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Response Options

## Slide 6
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Aerial observation

## Slide 7
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Aerial Observation
First response option
Collect key information about the spill:
  Confirm source;
  Scale of spill;
  Oil trajectory;
  Oil behaviour;
  Support equipment deployment; and
  Strategic planning

## Slide 8
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Aerial observation
Satellites, helicopter, fixed wing aircraft and unmanned aerial vehicles
Trained observers or sensors (UV, SLAR, IR, etc.)
Safety (twin engine aircraft)
Must relay information quickly to command centre

## Slide 9
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Aerial observation

## Slide 10
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Protection of Sensitive Resources

## Slide 11
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Protection of Sensitive Resources
Prevent contamination of important areas using booms
  Biological (e.g. marshes)
  Economic (e.g. marina)
Requires prioritization of sensitive resources
  Importance of sensitivity maps
Good use of limited resources (booms)
High benefits for low costs

## Slide 12
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Protection of Sensitive Resources
Limited by availability of booms
Limited by booms’ failure conditions
  Strong currents (more than 1 knot)
  Weather conditions (waves)
Limited protection for large sensitive areas
  Deployed boom length is limited
Requires maintenance once deployed
Effective response options for more sheltered nearshore environments

## Slide 13
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Protection of Sensitive Resources

## Slide 14
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
A few Words on Booms
Booms are an essential tool for oil spill response
  Shoreline protection and containment of oil
Many types of booms on the market
  Solid flotation vs. inflatable
  Offshore vs. nearshore
  Newer systems: ocean and current busters
Will fail in some conditions
  Strong currents (more than 1 knot)
  Weather conditions (waves)

## Slide 15
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Booms deployment requires substantial logistics
  Transportation (boats, trucks)
  Trained personnel
  Maintenance
A few Words on Booms

## Slide 16
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Containment and Recovery

## Slide 17
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Containment and Recovery
Objectives: stop spreading, concentrate and remove oil from the environment
Equipment required:
  Booms;
  Skimmer(s) with power pack;
  Vessel(s) to pull booms and transport equipment
  Storage tank for recovered oil/oily water
Significant investment up front
Substantial logistics

## Slide 18
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Containment and Recovery
Success is limited by:
  Weather conditions for booms operation (current, sea state)
  Deployment time
  Encounter rate with oil
  Storage capacity
  Debris
For larger offshore spills, containment and recovery of more than 10% may be difficult to achieve.

## Slide 19
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
A few Words on Skimmers
It is basically a floating pump
Many different types on the market
  Weir
  Oleophillic
  Vacuum
  Mechanical
Limitations:
  Oil type
  Sea state and weather
  Amount of debris
  Transport

## Slide 20
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Skimmers

## Slide 21
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Dispersants

## Slide 22
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Dispersants
Objective: Promote natural dispersion of oil into water column.
Dispersants are chemical products formulated to produce 10s-microns-size oil droplets that will be dispersed, diluted and eventually biodegraded in the environment.
New generations of dispersants have low toxicity and high efficiency.

## Slide 23
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Dispersants
How dispersants work
  Chemical formulation to reduce interfacial surface tension between oil and water
  Oil will form 10s-microns-size droplets because of mixing energy from waves
  Because of their small size, these droplets will remain suspended in water column as a plume
  Plume will be diluted by mixing energy and currents
  Increase biodegradation due to larger surface area for bacteria

## Slide 24
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Dispersants
Application by aircraft or boats
  Aircraft
    Plane or helicopter
    Wide coverage
    Trained pilots
  Boats
    Small local response

## Slide 25
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Dispersants

## Slide 26
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Dispersants
Issues with dispersants use
  Toxicity
    Dispersants have lower toxicity than dispersed oil
    Field test have shown higher oil concentrations in 0 to 10 m water depth
    Background oil concentration within hours
    Short duration exposure because of dilution
  Oil viscosity and dispersibility
    Readily dispersible for oil viscosity below 5,000cSt
    Moderate for oil viscosity between 5,000–10,000cSt
    Likely to be ineffective above 10,000cSt

## Slide 27
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Dispersants
Issues with dispersants use
  Oil viscosity and time
    Weathering processes will increase oil viscosity over time
    Dispersants must be applied before viscosity is too high
    “Window of opportunity”
  Sea state and weather
    Typically requires between 3 to 18 m/s wind speed and 0.5 to 5 m wave height
    Weather conditions must permit application of dispersants

## Slide 28
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Dispersants
Issues with dispersants use
  Government approval
    Usually required by national regulations
    List of approved dispersants
    Criteria for application
    Dispersants use policy
  Application zones
    Not in shallow water (less than 10 to 20 m)
    Not near water intakes
    Mainly offshore
    Net environmental benefit

## Slide 29
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Dispersants
Advantages
  Elimination of oil from sea surface
    Protection of birds and shoreline
  Improve biodegradation of oil
  Does not generate waste
  Quick response (if in contingency plan)
  Reasonable costs for potentially high benefits

## Slide 30
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
In situ burning

## Slide 31
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
In Situ Burning
Objective: Remove oil from sea surface by ignition
Required equipment:
  Vessels
  Fire resistant booms
Can eliminate significant quantity of oil rapidly
Minimize waste generation
Especially efficient for spill in ice

## Slide 32
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
In Situ Burning

## Slide 33
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
In Situ Burning
Issues with in situ burning
  Availability of fire resistant booms
  Oil thickness
    A minimum of 2 mm required to sustain burn
    If less than 2 mm, burning will stop
  Smoke plume
    Smoke = gas, CO2, particulates
    Avoid exposure to smoke
    Must be aware of sensitive resources that might be exposed to smoke plume

## Slide 34
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
In Situ Burning
Issues with in situ burning
  Oil weathering
    High viscosity oil can be harder to ignite
  Burn residue
    Heavy burn residue possible
    Can be difficult to recover and sink in some cases
  Safety
    Fire can spread to adjacent structures, vessels
    Exclusion zone
    Avoid exposure to smoke

## Slide 35
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
In Situ Burning

## Slide 36
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Clean-up

## Slide 37
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Clean-up
Objective: Remove oil from shoreline without causing additional damage
Various techniques available
  Natural
  Manual
  Mechanical
  Flooding/low pressure
  High pressure

## Slide 38
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Clean-up

## Slide 39
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Clean-up

## Slide 40
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Clean-up
Shoreline clean-up strategy
  Evaluation
    Survey (shoreline types, degree of oiling)
    Shoreline Clean-up Assessment Technique (SCAT) process
  Identify priorities
    amenity vs. environment
    response speed vs. aggressiveness
  Establish shoreline clean-up end-points
  Implement clean-up

## Slide 41
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Survey

## Slide 42
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Clean-up
Shoreline clean-up strategy
  Re-evaluate shoreline
    Does shoreline meets end-point criteria?
      If yes, stop
      If no, identify new method
    Must balance between aggressiveness and potential damages from clean-up

## Slide 43
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Shoreline Clean-up
Oil plentiful in the early stages:
  high volume of oil treatment
As clean-up brought to a close:
  very little oil remains
At some point the costs of oil treatment are disproportionate to the benefits
Clean-up Effort
Oil Treated

## Slide 44
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Identify priorities
    Protection of public
    Sensitivities
      Economic
      Social
      Environmental
Know your limiting factors
    Type of oil
    Weather and sea conditions
How to Select a Response Strategy?

## Slide 45
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Net Environmental Benefits
    Compare overall impacts of each response option against no intervention
    Select suite of response options that minimize overall impact
Do you have the necessary operational capacity?
    Command and control structure
    Availability of equipment/personnel
    Logistics and deployment time
Implement response strategy
Evaluate success and re-assess
How to Select a Response Strategy?

## Slide 46
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Conclusion
Various response options available for oil spills
None of these options are perfect
  each has benefits and limitations
You are likely to use a combination of methods
At the strategic level, you must know available options, their
benefits, limitations and impacts.

## Slide 47
CGPRT(W) : Ensuring Clean Seas and Coasts in Western Region ……
Any questions?